FIND2.COM DOCUMENTATION

Find2 is a public domain utility for the PC-8401A 
computer that intercepts the LST: device.  If a caret
(^) is sent to the BDOS LST: device followed immediately
by a left square bracket ([), these two characters are
replaced by the single ASCII ESC character.  

This program was written in response to the condition of
WordStar-to-go (in the PC-8401A) causing the imbedded ESC
character to be printed out as a caret and a left bracket
(^[) instead of the ASCII ESC.  PC-8401A users  that have
Non-NEC printers that utilize the ESC code for special 
printer effects could not obtain the full use of their 
printer without a LST: filter such as FIND2.  ESC can now 
be entered into WS by typing in ^[ (as well as CTRL-P ESC.)
Be sure to set the IPL to FIND2 once it is loaded in your
PC-8401A, becuase power-off to power-on transitions cause 
the BDOS table to be re-written, and therfore nullify this
program.  The SetIPL can be invoked from the PC-8401A MENU
OPTION key - SHIFT-F.2<RETURN>.  F.3 is the SetIPL option.
Press F.3 and respond to the "Type IPL command" prompt with
FIND2<RETURN>.  To produce a single caret (^) upon printout,
specify caret followed by accent grave (^`.)

As an added bonus this program will allow all control 
characters to be passed to the printer.  Simply precede 
the character you want turned into a control character
with a caret character.  The following chart displays
character input and resulting character output in Hex-
adecimal, Decimal and ASCII control-code names:

Input   Hex   Decimal  ASCII | Input    Hex   Decimal  ASCII 
 ^@	00	00	Nul  |  ^P	10	16	Dle
 ^A	01	01	Soh  |  ^Q	11	17	Dc1
 ^B	02	02	Stx  |  ^R	12	18	Dc2
 ^C	03	03	Etx  |  ^S	13	19	Dc3
 ^D	04	04	Eot  |  ^T	14	20	Dc4
 ^E	05	05	Enq  |  ^U	15	21	Nak
 ^F	06	06	Ack  |  ^V	16	22	Syn
 ^G	07	07	Bel  |  ^W	17	23	Etb
 ^H	08	08	Bs   |  ^X	18	24	Can
 ^I	09	09	Ht   |  ^Y	19	25	Em
 ^J	0A	10	Lf   |  ^Z	1A	26	Sub
 ^K	0B	11	Vt   |  ^[	1B	27	Esc
 ^L	0C	12	Ff   |  ^\	1C	28	Fs
 ^M	0D	13	Cr   |  ^]	1D	29	Gs
 ^N	0E	14	So   |  ^^	1E	30	Rs
 ^O	0F	15	Si   |  ^_	1F	31	Us

Input:
Caret Space(^ ) through Caret Question Mark (^?) and then
Caret Acent Grave (^`) through Caret Tilde (^~) on the ASCII 
chart are undefined and will result in a printable caret (^) 
being produced only.

Example use in WS-to-go:
My printer requires an ESC Q to enter Condensed character printing 
mode, an ESC N to return to normal Pica mode, a 0E hexadecimal
to enter Enlarged character printing mode and a 15 decimal to return
to normal sized printing.  I can use the following:

^[QThis prints condensed characters ^[NNow they are pica sized.
^NThese pica characters will be enlarged ^OThese will be normal sized.
^ ^!^"^#^$^%^&^'^(^)^*^+^,^-^.^/^0^1^2^3^4^5^6^7^8^9^:^;^<^=^>^?
The above line produces 32 caret characters only.
^`^a^b^c^d^e^f^g^h^i^j^k^l^m^n^o^p^q^r^s^t^u^v^w^x^y^z^{^|^}^~
The above line produces 31 caret characters only.
This produces a backspace (control-h) such as to accent a vowel :
e^H'
(A printer such as the PC-8023 must be in incremental rather than
logic seeking mode to print a literal backspace.)
FILE END.