AX25.DOC

         AX.25 Amateur Packet-Radio Link-Layer Protocol
                    Version 2.0  October 1984

Copyright (c) 1984 by

The American Radio Relay Legue, Inc.

Blanket permission to copy this publication by end users for 
noncommercial purposes is hereby granted.  No part of this
work may be reproduced in any form where such copy is offered
in exchange for any payment unless written permission has first
been secured from the publisher.

2.  AX.25 Link-Layer Protocol Specification

2.1  Scope and Field of Operation

        In  order  to  provide  a  mechanism  for  the   reliable 
transport  of  data  between  two  signaling  terminals,  it   is 
necessary  to define a protocol that can accept and deliver  data 
over a variety of types of communications links.  The AX.25 Link-
Layer  Protocol is designed to provide this service,  independent 
of any other level that may or may not exist.

        This protocol conforms to ISO Recommendations 3309,  4335 
(including DAD 1&2) and 6256 high-level data link control  (HDLC) 
and  uses  some terminology found in these  documents.   It  also 
conforms with ANSI X3.66, which describes ADCCP, balanced mode.

        This  protocol  follows,  in principle,  the  CCITT  X.25 
Recommendation,  with the exception of an extended address  field 
and  the addition of the Unnumbered Information (UI)  frame.   It 
also follows the principles of CCITT Recommendation Q.921  (LAPD) 
in the use of multiple links, distinguished by the address field, 
on a single shared channel.

        As  defined,  this  protocol will work  equally  well  in 
either half- or full-duplex Amateur Radio environments.

        This protocol has been designed to work equally well  for 
direct  connections between two individual  amateur  packet-radio 
stations or an individual station and a multiport controller.

        This  protocol allows for the establishment of more  than 
one  link-layer  connection  per  device, if  the  device  is  so 
capable.

        This  protocol  does not  prohibit  self-connections.   A 
self-connection  is considered to be when a device establishes  a 
link  to  itself using its own address for both  the  source  and 
destination of the frame.

        Most  link-layer  protocols assume that one  primary  (or 
master)  device  (generally  called  a  DCE,  or  data   circuit-
terminating equipment) is connected to one or more secondary  (or 
slave)  device(s)  (usually  called a DTE,  or  data  terminating 
equipment).   This type of unbalanced operation is not  practical 
in a shared-RF Amateur Radio environment.  Instead, AX.25 assumes 
that  both  ends  of  the link are of  the  same  class,  thereby 
eliminating  the two different classes of devices.  The term  DXE 
is  used in this protocol specification to describe the  balanced Štype of device found in amateur packet radio.

2.2  Frame Structure

        Link  layer packet radio transmissions are sent in  small 
blocks of data, called frames.  Each frame is made up of  several 
smaller groups, called fields.  Fig.1 shows the three basic types 
of  frames.  Note that the first bit to be transmitted is on  the 
left side.



        First
        Bit Sent

          Flag      Address     Control     FCS      Flag
        01111110  112/560 Bits  8 Bits    16 Bits  01111110

                Fig. 1A -- U and S frame construction



        First
        Bit Sent

 Flag      Address      Control    PID    Info.       FCS      Flag
 01111110  112/560 Bits   8 Bits   8 Bits  N*8 Bits   16 Bits  01111110

                Fig. 1B -- Information frame construction



        Each field is made up of an integral number of octets (or 
bytes), and serves a specific function as outlined below.

2.2.1  Flag Field

        The flag field is one octet long.  Since the flag is used 
to  delimit  frames, it occurs at both the beginning and  end  of 
each  frame.  Two frames may share one flag, which  would  denote 
the  end of the first frame, and the start of the next frame.   A 
flag consists of a zero followed by six ones followed by  another 
zero,  or  01111110 (7E hex).  As a result of bit  stuffing  (see 
2.2.6,  below),  this sequence is not allowed to  occur  anywhere 
else inside a complete frame.

2.2.2  Address Field

        The address field is used to identify both the source  of 
the  frame and its destination.  In addition, the  address  field 
contains  the  command/response information  and  facilities  for 
level 2 repeater operation.  

        The encoding of the address field is described in 2.2.13.
Š2.2.3  Control Field

        The  control field is used to identify the type of  frame 
being  passed  and  control several attributes  of  the  level  2 
connection.   It  is  one octet in length, and  its  encoding  is 
discussed in 2.3.2.1, below.

2.2.4  PID Field

        The  Protocol  Identifier  (PID) field  shall  appear  in 
information  frames (I and UI) only.  It identifies what kind  of 
layer 3 protocol, if any, is in use.

        The PID itself is not included as part of the octet count 
of the information field.  The encoding of the PID is as follows:



  M      L
  S      S 
  B      B
  yy01yyyy AX.25 layer 3 implemented.
  yy10yyyy AX.25 layer 3 implemented.
  11001100 Internet Protocol datagram layer 3 implemented.
  11001101 Address resolution protocol layer 3 implemented.
  11110000 No layer 3 implemented.
  11111111 Escape character.  Next octet contains more Level 3
           protocol information.



        Where:

        A y indicates all combinations used.

        Note:

        All  forms  of  yy11yyyy and yy00yyyy  other  than  those 
listed  above  are  reserved  at this time  for  future  level  3 
protocols.   The  assignment of these formats is  up  to  amateur 
agreement.   It  is  recommended that the  creators  of  level  3 
protocols   contact  the  ARRL  Ad  Hoc  Committee   on   Digital 
Communications for suggested encodings.

2.2.5  Information Field

        The  information field is used to convey user  data  from 
one  end of the link to the other.  I fields are allowed in  only 
three  types of frames:  the I frame, the UI frame, and the  FRMR 
frame.   The  I  field can be up to 256 octets  long,  and  shall 
contain  an integral number of octets.  These  constraints  apply 
prior to the insertion of zero bits as specified in 2.2.6, below.  
Any  information  in the I field shall be passed along  the  link 
transparently,  except  for the zero-bit  insertion  (see  2.2.6) 
necessary  to prevent flags from accidentally appearing in the  I Šfield.

2.2.6  Bit Stuffing

        In  order to assure that the flag bit sequence  mentioned 
above  doesn't appear accidentally anywhere else in a frame,  the 
sending  station  shall monitor the bit sequence for a  group  of 
five  or more contiguous one bits.  Any time five contiguous  one 
bits  are sent the sending station shall insert a zero bit  after 
the  first  one  bit.   During frame  reception,  any  time  five 
contiguous  one  bits  are  received,  a  zero  bit   immediately 
following five one bits shall be discarded.

2.2.7  Frame-Check Sequence

        The  frame-check sequence (FCS) is a  sixteen-bit  number 
calculated  by  both the sender and receiver of a frame.   It  is 
used  to  insure that the frame was not corrupted by  the  medium 
used to get the frame from the sender to the receiver.  It  shall 
be calculated in accordance with ISO 3309 (HDLC) Recommendations.

2.2.8  Order of Bit Transmission

        With  the  exception of the FCS field, all fields  of  an 
AX.25 frame shall be sent with each octet's least-significant bit 
first.  The FCS shall be sent most-significant bit first.

2.2.9  Invalid Frames

        Any frame consisting of less than 136 bits (including the 
opening  and closing flags), not bounded by opening  and  closing 
flags, or not octet aligned (an integral number of octets), shall 
be  considered  an  invalid frame by the link  layer.   See  also 
2.4.4.4, below.

2.2.10  Frame Abort

        If a frame must be prematurely aborted, at least  fifteen 
contiguous ones shall be sent with no bit stuffing added.

2.2.11  Interframe Time Fill

        Whenever   it  is  necessary  for  a  DXE  to  keep   its 
transmitter  on  while  not actually  sending  frames,  the  time 
between frames should be filled with contiguous flags.

2.2.12  Link Channel States

        Not applicable.

2.2.13  Address-Field Encoding

        The  address  field of all frames shall be  encoded  with 
both the destination and source amateur call signs for the frame.  
Except  for the Secondary Station Identifier (SSID), the  address Šfield  should  be made up of upper-case alpha and  numeric  ASCII 
characters only.  If level 2 amateur "repeaters" are to be  used, 
their call signs shall also be in the address field.

        The  HDLC address field is extended beyond one  octet  by 
assigning  the  least-significant  bit of each  octet  to  be  an 
"extension bit".  The extension bit of each octet is set to zero, 
to indicate the next octet contains more address information,  or 
one,  to  indicate  this is the last octet of  the  HDLC  address 
field.   To make room for this extension bit, the  amateur  Radio 
call sign information is shifted one bit left.

2.2.13.1  Nonrepeater Address-Field Encoding

        If  level  2 repeaters are not being  used,  the  address 
field is encoded as shown in Fig. 2.  The destination address  is 
the call sign and SSID of the amateur radio station to which  the 
frame is addressed, while the source address contains the amateur 
call  sign  and SSID of the station that sent the  frame.   These 
call signs are the call signs of the two ends of a level 2  AX.25 
link only.



        First
        Octet Sent

                     Address Field of Frame
        Destination Address         Source Address
        A1 A2 A3 A4 A5 A6 A7    A8 A9 A10 A11 A12 A13 A14

        Fig. 2 -- Nonrepeater Address-Field Encoding



        A1  through A14 are the fourteen octets that make up  the 
two  address  subfields of the address  field.   The  destination 
subaddress is seven octets long (A1 thru A7), and is sent  first.  
This  address sequence provides the receivers of frames  time  to 
check  the  destination address subfield to see if the  frame  is 
addressed to them while the rest of the frame is being  received.  
The  source  address subfield is then sent in octets  A8  through 
A14.   Both  of these subfields are encoded in the  same  manner, 
except  that  the last octet of the address field  has  the  HDLC 
address extension bit set.

        There  is  an octet at the end of each  address  subfield 
that contains the Secondary Station Identifier (SSID).  The  SSID 
subfield  allows an Amateur Radio operator to have more than  one 
packet-radio station operating under the same call sign.  This is 
useful when an amateur wants to put up a repeater in addition  to 
a regular station, for example.  The C bits (see 2.4.1.2,  below) 
and H bit (see 2.2.13.2, below) are also contained in this octet, 
along with two bits which are reserved for future use.
Š        Fig.  3A shows a typical AX.25 frame in  the  nonrepeater 
mode of operation.



        Octet   ASCII   Bin.Data  Hex Data

        Flag            01111110     7E
         A1       K     10010110     96
         A2       8     01110000     70
         A3       M     10011010     9A
         A4       M     10011010     9A
         A5       O     10011110     9E
         A6     space   01000000     40
         A7     SSID    11100000     E0
         A8       W     10101110     AE
         A9       B     10000100     84
         A10      4     01100100     68
         A11      J     10010100     94
         A12      F     10001100     8C
         A13      I     10010010     92
         A14    SSID    01100001     61
       Control    I     00111110     3E
         PID    none    11110000     F0
         FCS    part 1  XXXXXXXX     HH
         FCS    part 2  XXXXXXXX     HH
        Flag            01111110     7E

        Bit position    76543210

      Fig. 3A -- Nonrepeater AX.25 frame



        The frame shown is an I frame, not going through a  level 
2 repeater, from WB4JFI (SSID=0) to K8MMO (SSID=0), with no level 
3  protocol.   The P/F bit is set; the  receive  sequence  number 
(N(R)) is 1; the send sequence number (N(S)) is 7.

2.2.13.1.1  Destination Subfield Encoding

        Fig.  3 shows how an amateur call sign is placed  in  the 
destination address subfield, occupying octets A1 thru A7.



             Octet   ASCII   Bin.Data   Hex Data

              A1       W     10101110      AE
              A2       B     10000100      84
              A3       4     01101000      68
              A4       J     10010100      94
              A5       F     10001100      8C
              A6       I     10010010      92
              A7     SSID    CRRSSID0Š
           Bit Position-->   76543210

          Fig. 3 -- Destination Field Encoding



        Where:

        1.  The top octet (A1) is the first octet sent, with  bit 
            0  of each octet being the first bit sent, and bit  7 
            being the last bit sent.

        2.  The  first (low-order or bit 0) bit of each octet  is 
            the HDLC address extension bit, which is set to  zero 
            on all but the last octet in the address field, where 
            it is set to one.

       3.   The  bits marked "r" are reserved bits.  They may  be 
            used in an agreed-upon manner in individual networks.  
            When not implemented, they should be set to one.

        4.  The  bit marked "C" is used as  the  command/response 
            bit of an AX.25 frame, as outlined in 2.4.1.2 below.

        5.  The  characters of the call sign should  be  standard 
            seven-bit  ASCII  (upper  case only)  placed  in  the 
            leftmost seven bits of the octet to make room for the 
            address  extension  bit.  If the call  sign  contains 
            fewer  than six characters, it should be padded  with 
            ASCII spaces between the last call sign character and 
            the SSID octet.

        6.  The  0000  SSID is reserved for  the  first  personal 
            AX.25 station. This establishes one standard SSID for 
            "normal" stations to use for the first station.

2.2.13.2  Level 2 Repeater-Address Encoding

        If  a  frame  is to go through  level  2  amateur  packet 
repeater(s), there is an additional address subfield appended  to 
the end of the address field.  This additional subfield  contains 
the call sign(s) of the repeater(s) to be used.  This allows more 
than one repeater to share the same RF channel.  If this subfield 
exists,  the  last octet of the source subfield has  its  address 
extension  bit  set to zero, indicating that  more  address-field 
data  follows.  The repeater-address subfield is encoded  in  the 
same  manner  as the destination and  source  address  subfields, 
except for the most-significant bit in the last octet, called the 
"H" bit.  The H bit is used to indicate whether a frame has  been 
repeated or not.

        In  order  to provide some method of  indicating  when  a 
frame has been repeated, the H bit is set to zero on frames going 
to  a repeater.  The repeater will set the H bit to one when  the Šframe  is retransmitted.  Stations should monitor the H bit,  and 
discard  any frames going to the repeater (uplink frames),  while 
operating  through  a repeater.  Fig. 4 shows how  the  repeater- 
address subfield is encoded.  Fig. 4A is an example of a complete 
frame after being repeated.



                Octet   ASCII   Bin.Data  Hex Data

                 A15      W     10101110     AE
                 A16      B     10000100     84
                 A17      4     01101000     68
                 A18      J     10010100     94
                 A19      F     10001100     8C
                 A20      I     10010010     92
                 A21    SSID    HRRSSID1

              Bit Order  -->    76543210

              Fig. 4 -- Repeater-address encoding



   Where:

   1.  The  top octet is the first octet sent, with bit  0  being 
       sent first and bit 7 sent last of each octet.

   2.  As  with  the  source and  destination  address  subfields 
       discussed  above, bit 0 of each octet is the HDLC  address 
       extension  bit, which is set to zero on all but  the  last 
       address octet, where it is set to one.

   3.  The  "R"  bits are reserved in the same manner as  in  the 
       source and destination subfields.

   4.  The  "H" bit is the has-been-repeated bit.  It is  set  to 
       zero  whenever a frame has not been repeated, and  set  to 
       one by the repeater when the frame has been repeated.



        Octet    ASCII   Bin.Data  Hex Data

        Flag             01111110     7E
         A1        K     10010110     96
         A2        8     01110000     70
         A3        M     10011010     9A
         A4        M     10011010     9A
         A5        O     10011110     9E
         A6      space   01000000     40
         A7      SSID    11100000     E0
         A8        W     10101110     AE
         A9        B     10000100     84Š         A10       4     01101000     68
         A11       J     10010100     94
         A12       F     10001100     8C
         A13       I     10010010     92
         A14     SSID    01100000     60
         A15       W     10101110     AE
         A16       B     10000100     84
         A17       4     01101000     68
         A18       J     10010100     94
         A19       F     10001100     8C
         A20       I     10010010     92
         A21     SSID    11100011     E3
       Control     I     00111110     3F
         PID     none    11110000     F0
         FCS     part 1  XXXXXXXX     HH
         FCS     part 2  XXXXXXXX     HH
        Flag             01111110     7E

        Bit position     76543210

      Fig. 4A -- AX.25 frame in repeater mode



        The  above frame is the same as Fig. 3A, except  for  the 
addition of a repeater-address subfield (WB4JFI, SSID=1).  The  H 
bit is set, indicating this is from the output of the repeater.

2.2.13.3 Multiple Repeater Operation

        The  link-layer AX.25 protocol allows  operation  through 
more  than  one  repeater, creating  a  primitive  frame  routing 
mechanism.   Up to eight repeaters may be used by  extending  the 
repeater-address subfield.  When there is more than one  repeater 
address,  the repeater address immediately following  the  source 
address  subfield  will be considered the address  of  the  first 
repeater  of  a multiple-repeater chain.  As a  frame  progresses 
through  a chain of repeaters, each successive repeater will  set 
the  H bit (has-been-repeated bit) in its SSID octet,  indicating 
that  the  frame has been successfully repeated through  it.   No 
other  changes  to the frame are made (except for  the  necessary 
recalculation of the FCS).  The destination station can determine 
the  route  the frame took to each it by  examining  the  address 
field.

        The  number of repeater addresses is variable.   All  but 
the last repeater address will have the address extension bits of 
all  octets  set to zero, as will all but the  last  octet  (SSID 
octet) of the last repeater address.  The last octet of the  last 
repeater address will have the address extension bit set to  one, 
indicating the end of the address field.

        It should be noted that various timers (see 2.4.7, below) 
may  have  to be adjusted to accommodate  the  additional  delays 
encountered  when a frame must pass through  a  multiple-repeater Šchain,  and  the return acknowledgement must travel  through  the 
same path before reaching the source device.

        It  is anticipated that multiple-repeater operation is  a 
temporary method of interconnecting stations over large distances 
until  such  time that a layer 3 protocol is in use.   Once  this 
layer 3 protocol becomes operational, repeater chaining should be 
phased out.

2.3  Elements of Procedure

2.3.1  
     The  elements of procedure are defined in terms  of  actions 
that occur on receipt of frames.

2.3.2  Control-Field Formats and State Variables

2.3.2.1  Control-Field Formats

        The control field is responsible for identifying the type 
of  frame  being sent, and is also used to  convey  commands  and 
responses  from  one  end of the link to the other  in  order  to 
maintain proper link control.

        The  control  fields  used in AX.25 use  the  CCITT  X.25 
control fields for balanced operation (LAPB), with an  additional 
control field taken from ADCCP to allow connectionless and round-
table operation.

        There are three general types of AX.25 frames.  They  are 
the Information frame (I frame), the Supervisory frame (S frame), 
and  the  Unnumbered  frame (U frame).  Fig. 5  shows  the  basic 
format  of  the  control field associated  with  these  types  of 
frames.



              Control-Field      Control-Field Bits
                  Type         7  6  5  4  3  2  1  0
  
                I Frame          N(R)   P    N(S)   0
                S Frame          N(R)  P/F S  S  0  1
                U Frame        M  M  M P/F M  M  1  1

                  Fig. 5 -- Control-field formats



        Where:

        1.  Bit 0 is the first bit sent and bit 7 is the last bit 
            sent of the control field.

        2.  N(S) is the send sequence number (bit 1 is the LSB).
Š        3.  N(R)  is  the receive sequence number (bit 5  is  the 
            LSB).

        4.  The  "S" bits are the supervisory function bits,  and 
            their encoding is discussed in 2.3.4.2.

        5.  The  "M" bits are the unnumbered frame modifier  bits 
            and their encoding is discussed in 2.3.4.3.

        6.  The  P/F bit is the Poll/Final bit.  Its function  is 
            described in 2.3.3.  The distinction between  command 
            and response, and therefore the distinction between P 
            bit and F bit, is made by addressing rules  discussed 
            in 2.4.1.2.

2.3.2.1.1  Information-Transfer Format

        All I frames have bit 0 of the control field set to zero.  
N(S)  is  the sender's send sequence number  (the  send  sequence 
number  of  this frame).  N(R) is the sender's  receive  sequence 
number (the sequence number of the next expected received frame).  
These numbers are described in 2.3.2.4.  In addition, the P/F bit 
is to be used as described in 2.4.2.  


2.3.2.1.2  Supervisory Format

        Supervisory  frames  are denoted by having bit 0  of  the 
control  field set to one, and bit 1 of the control field set  to 
zero.   S  frames  provide  supervisory  link  control  such   as 
acknowledging or requesting retransmission of I frames, and link-
level window control.  Since S frames do not have an  information 
field,  the  sender's send variable and  the  receiver's  receive 
variable are not incremented for S frames.  In addition, the  P/F 
bit is used as described in 2.4.2.

2.3.2.1.3  Unnumbered Format

        Unnumbered frames are distinguished by having both bits 0 
and 1 of the control field set to one.  U frames are  responsible 
for  maintaining additional control over the link beyond what  is 
accomplished  with  S  frames.  They  are  also  responsible  for 
establishing  and  terminating link connections.  U  frames  also 
allow  for the transmission and reception of information  outside 
of   the  normal  flow  control.   Some  U  frames  may   contain 
information and PID fields.  The P/F bit is used as described  in 
2.4.2.

2.3.2.2  Control-Field Parameters

2.3.2.3  Sequence Numbers

        Every  AX.25  I  frame shall be  assigned,  modulo  8,  a 
sequential  number  from  0 to 7.  This will allow  up  to  seven 
outstanding I frames per level 2 connection at a time.Š
2.3.2.4  Frame Variables and Sequence Numbers

2.3.2.4.1  Send State Variable V(S)

        The send state variable is a variable that is internal to 
the  DXE  and  is never sent.  It contains  the  next  sequential 
number  to  be assigned to the next transmitted  I  frame.   This 
variable is updated upon the transmission of each I frame.

2.3.2.4.2  Send Sequence Number N(S)

        The send sequence number is found in the control field of 
all  I  frames.  It contains the sequence number of the  I  frame 
being sent.  Just prior to the transmission of the I frame,  N(S) 
is updated to equal the send state variable.
  

2.3.2.4.3 Receive State Variable V(R)

        The receive state variable is a variable that is internal 
to the DXE.  It contains the sequence number of the next expected 
received I frame.  This variable is updated upon the reception of 
an  error-free  I  frame whose send sequence  number  equals  the 
present received state variable value.

2.3.2.4.4  Received Sequence Number N(R)

        The  received sequence number is in both I and S  frames.  
Prior  to  sending an I or S frame, this variable is  updated  to 
equal  that  of  the received  state  variable,  thus  implicitly 
acknowledging  the  proper  reception of all  frames  up  to  and 
including N(R)-1.

2.3.3  Functions of Poll/Final (P/F) Bit

        The  P/F bit is used in all types of frames.  It is  used 
in  a  command  (poll) mode to request an immediate  reply  to  a 
frame.   The  reply  to this poll is  indicated  by  setting  the 
response  (final)  bit  in  the  appropriate  frame.   Only   one 
outstanding  poll condition per direction is allowed at  a  time.  
The procedure for P/F bit operation is described in 2.4.2.

2.3.4  Control Field Coding for Commands and Responses

        The following commands and responses, indicated by  their 
control field encoding, are to be use by the DXE:

2.3.4.1  Information Command Frame Control Field

        The  function  of  the  information  (I)  command  is  to 
transfer   across  a  data  link  sequentially  numbered   frames 
containing an information field.

        The  information-frame control field is encoded as  shown Šin  Fig. 6.  These frames are sequentially numbered by  the  N(S) 
subfield to maintain control of their passage over the link-layer 
connection.



                          Control Field Bits
                           7 6 5 4 3 2 1 0
                            N(R) P  N(S) 0

                    Fig. 6 -- I frame control field



2.3.4.2  Supervisory Frame Control Field

        The supervisory frame control fields are encoded as shown 
in Fig. 7.



        Control Field Bits       7   6   5   4   3   2   1   0
        Receive Ready     RR        N(R)    P/F  0   0   0   1
        Receive Not Ready RNR       N(R)    P/F  0   1   0   1
        Reject            REJ       N(R)    P/F  1   0   0   1

                Fig. 7 -- S frame control fields


                          The Frame identifiers:

C or SABM          Layer 2 Connect Request
D or DISC          Layer 2 Disconnect Request
I                  Information Frame
RR                 Receive Ready. System Ready To Receive
RNR or NR          Receive Not Ready. TNC Buffer Full
RJ or REJ          Reject Frame. Out of Sequence or Duplicate
FRMR               Frame Reject. Fatal Error
UI                 Unnumbered Information Frame. "Unproto"
DM                 Disconnect Mode. System Busy or Disconnected.


2.3.4.2.1  Receive Ready (RR) Command and Response

        Receive Ready is used to do the following:

   1.  to  indicate  that the sender of the RR is  now  able  to 
       receive more I frames.

   2.  to  acknowledge  properly  received I frames  up  to,  and 
       including N(R)-1, and

   3.  to clear a previously set busy condition created by an RNR 
       command having been sent.
Š        The status of the DXE at the other end of the link can be 
requested  by  sending a RR command frame with the P-bit  set  to 
one.

2.3.4.2.2  Receive Not Ready (RNR) Command and Response

        Receive Not Ready is used to indicate to the sender of  I 
frames  that  the receiving DXE is temporarily  busy  and  cannot 
accept any more I frames.  Frames up to N(R)-1 are  acknowledged.  
Any I frames numbered N(R) and higher that might have been caught 
between states and not acknowledged when the RNR command was sent 
are not acknowledged.

        The RNR condition can be cleared by the sending of a  UA, 
RR, REJ, or SABM frame.

        The status of the DXE at the other end of the link can be 
requested  by sending a RNR command frame with the P bit  set  to 
one.

2.3.4.2.3  Reject (REJ) Command and Response

        The  reject frame is used to request retransmission of  I 
frames  starting  with N(R).  Any frames that were  sent  with  a 
sequence number of N(R)-1 or less are acknowledged.  Additional I 
frames may be appended to the retransmission of the N(R) frame if 
there are any.

        Only  one  reject  frame condition  is  allowed  in  each 
direction  at  a time.  The reject condition is  cleared  by  the 
proper  reception of I frames up to the I frame that  caused  the 
reject condition to be initiated.

        The status of the DXE at the other end of the link can be 
requested  by sending a REJ command frame with the P bit  set  to 
one.

2.3.4.3  Unnumbered Frame Control Fields

        Unnumbered  frame control fields are either  commands  or 
responses.

        Fig.  8 shows the layout of U frames  implemented  within 
this protocol.



        Control Field                Type     Control Field Bits
                                            7  6  5  4  3  2  1  0

Set Asynchronous Balanced Mode-SABM  Cmd    0  0  1  P  1  1  1  1
Disconnect-DISC                      Cmd    0  1  0  P  0  0  1  1
Disconnected Mode-DM                 Res    0  0  0  F  1  1  1  1
Unnumbered Acknowledge-UA            Res    0  1  1  F  0  0  1  1
Frame Reject-FRMR                    Res    1  0  0  F  0  1  1  1ŠUnnumbered Information-UI           Either  0  0  0 P/F 0  0  1  1

                Fig. 8 -- U frame control fields



2.3.4.3.1  Set Asynchronous Balanced Mode (SABM) Command

        The  SABM  command  is  used  to  place  2  DXEs  in  the 
asynchronous balanced mode.  This is a balanced mode of operation 
known as LAPB where both devices are treated as equals.

        Information fields are not allowed in SABM commands.  Any 
outstanding  I frames left when the SABM command is  issued  will 
remain unacknowledged.

        The  DXE  confirms  reception and acceptance  of  a  SABM 
command   by  sending  a  UA  response  frame  at  the   earliest 
opportunity.   If  the  DXE is not capable of  accepting  a  SABM 
command, it should respond with a DM frame if possible.

2.3.4.3.2  Disconnect (DISC) Command

        The  DISC  command is used to terminate  a  link  session 
between  two  stations.  No information field is permitted  in  a 
DISC command frame.

        Prior  to  acting on the DISC frame,  the  receiving  DXE 
confirms acceptance of the DISC by issuing a UA response frame at 
its  earliest opportunity.  The DXE sending the DISC  enters  the 
disconnected state when it receives the UA response.

        Any  unacknowledged  I frames left when this  command  is 
acted upon will remain unacknowledged.