2.3.4.3.3  Frame Reject (FRMR) Response

2.3.4.3.3.1  
     The FRMR response frame is sent to report that the  receiver 
of  a frame cannot successfully process that frame and  that  the 
error condition is not correctable by sending the offending frame 
again.  Typically this condition will appear when a frame without 
an  FCS  error  has  been received  with  one  of  the  following 
conditions:

 1.  The  reception of an invalid or not implemented  command  or 
     response frame.

 2.  The reception of an I frame whose information field  exceeds 
     the agreed-upon length.  (See 2.4.7.3, below.)

 3.  The  reception  of an improper N(R).  This  usually  happens 
     when the N(R) frame has already been sent and  acknowledged, 
     or when N(R) is out of sequence with what was expected.
Š 4.  The reception of a frame with an information field where one 
     is  not  allowed, or the reception of a U or S  frame  whose 
     length is incorrect.  Bits W and Y described in  2.3.4.3.3.2 
     should both be set to one to indicate this condition.

      5.  The reception of a supervisory frame with the F bit set 
     to  one,  except  during a  timer  recovery  condition  (see 
     2.4.4.9), or except as a reply to a command frame sent  with 
     the  P  bit  set to one. Bit W  (described  in  2.3.4.3.3.2) 
     should be set to one.

 6.  The reception of an unexpected UA or DM response frame.  Bit 
     W should be set to one.

 7.  The reception of a frame with an invalid N(S).  Bit W should be
     set to one.

        An  invalid N(R) is defined as one which points to  an  I 
frame  that previously has been transmitted and acknowledged,  or 
an  I  frame which has not been transmitted and is not  the  next 
sequential I frame pending transmission.
  
        An  invalid N(S) is defined as an N(S) that is  equal  to 
the  last transmitted N(R)+k and is equal to the  received  state 
variable  V(R),  where  k is the maximum  number  of  outstanding 
information frames as defined in 2.4.7.4 below.

        An  invalid  or not implemented command  or  response  is 
defined  as a frame with a control field that is unknown  to  the 
receiver of this frame.

2.3.4.3.3.2  
     When a FRMR frame is sent, an information field is added  to 
the  frame that contains additional information indicating  where 
the  problem  occurred.  This information field is  three  octets 
long and is shown in Fig. 9.



                     Information Field Bits
 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
  0  0  0  0  Z  Y  X  W   V(R)    C   V(S)  0  Rejected Frame 
                                   R            Control Field

             Fig. 9 -- FRMR frame information field



  Where:

  1.  The rejected frame control field carries the control  field 
      of  the frame that caused the reject condition.  It  is  in 
      bits 0-7 of the information field.

  2.  V(S)  is  the  current send state variable  of  the  device Š      reporting the rejection (bit 9 is the low bit).

  3.  The  CR bit is set to zero to indicate the  rejected  frame 
      was a command, or one if it was a response.

  4.  V(R)  is the current receive state variable of  the  device 
      reporting rejection (bit 13 is the low bit).

  5.  If W is set to 1, the control field received was invalid or 
      not implemented.

  6.  If  X  is  set  to 1, the  frame  that  caused  the  reject 
      condition  was considered invalid because it was a U  or  S 
      frame  that had an information field that is  not  allowed.  
      Bit W must be set to 1 in addition to the X bit.

  7.  If  Y is set to 1, the control field received and  returned 
      in   bits   exceeded  the  maximum   allowed   under   this 
      recommendation in 2.4.7.3, below.

  8.  If  A is set to 1, the control field received and  returned 
      in bits 1 to 8 contained an invalid N(R).

  9.  Bits 8, and 20 to 23 are set to 0.


2.3.4.3.4  Unnumbered Acknowledge (UA) Response

        The  UA  response  frame  is  sent  to  acknowledge   the 
reception  and  acceptance of a SABM or DISC  command  frame.   A 
received command is not actually processed until the UA  response 
frame  is  sent.  Information fields are not permitted  in  a  UA 
frame.

2.3.4.3.5  Disconnected Mode (DM) Response

        The  disconnected  mode response is sent whenever  a  DXE 
receives  a  frame  other  than a SABM or UI  frame  while  in  a 
disconnected  mode.   It  is  also sent to  request  a  set  mode 
command,  or  to indicate it cannot accept a  connection  at  the 
moment.  The DM response does not have an information field.

        Whenever a SABM frame is a received, and it is determined 
that  a  connection is not possible, a DM frame  shall  be  sent.  
This  will  indicate  that the called  station  cannot  accept  a 
connection at that time.

        While a DXE is in the disconnected mode, it will  respond 
to  any command other than a SABM or UI frame with a DM  response 
with the P/F bit set to 1.

2.3.4.3.6  Unnumbered Information (UI) Frame

        The   Unnumbered  Information  frame  contains  PID   and 
information fields and is used to pass information along the link Šoutside the normal information controls.  This allows information 
fields  to go back and forth on the link bypassing flow  control.  
Since   these  frames  are  not  acknowledgeable,  if  one   gets 
obliterated, there is no way to recover it.  A received UI  frame 
with  the  P bit set shall cause a response  to  be  transmitted.  
This response shall be a DM frame when in the disconnected  state 
or  a  RR  (or  RNR, if appropriate)  frame  in  the  information 
transfer state.

2.3.5  Link Error Reporting and Recovery

        There are several link-layer errors that are  recoverable 
without  terminating the connection.  These error situations  may 
occur  as  a  result  of  malfunctions  within  the  DXE,  or  if 
transmission errors occur.

2.3.5.1  DXE Busy Condition

        When  a  DXE  becomes temporarily  unable  to  receive  I 
frames,  such  as when receive buffers are full, it will  send  a 
Receive Not Ready (RNR) frame.  This informs the other DXE   that 
this  DXE  cannot handle any more I frames at the  moment.   This 
condition is usually cleared by the sending of a UA, RR, REJ,  or 
SABM command frame.

2.3.5.2  Send Sequence Number Error

        If the send sequence number, N(S), of an otherwise error-
free  received frame does not match the receive  state  variable, 
V(R),  a  send sequence error has occurred, and  the  information 
field will be discarded.  The receiver will not acknowledge  this 
frame, or any other I frames, until N(S) matches V(R).  

        The  control  field of the erroneous I frame(s)  will  be 
accepted so that link supervisory functions such as checking  the 
P/F  bit can still be performed.  Because of this  updating,  the 
retransmitted I frame may have an updated P bit and N(R).

2.3.5.3  Reject (REJ) Recovery

        REJ  is  used  to request a retransmission  of  I  frames 
following  the  detection  of a N(S) sequence  error.   Only  one 
outstanding  "sent  REJ" condition is allowed at  a  time.   This 
condition  is  cleared  when  the  requested  I  frame  has  been 
received.

        A DXE receiving the REJ command will clear the  condition 
by  resending all outstanding I frames (up to the  window  size), 
starting with the one indicated in N(R) of the REJ frame.

2.3.5.4  Time-out Error Recovery

2.3.5.4.1  T1 Timer Recovery

        If  a DXE, due to a transmission error, does not  receive Š(or  receives and discards) a single I frame or the last I  frame 
in  a sequence of I frames, it will not detect  a  send-sequence-
number  error,  and therefore will not transmit a REJ.   The  DXE 
which transmitted the unacknowledged I frame(s) shall,  following 
the  completion of time-out period T1, take appropriate  recovery 
action  to determine when I frame retransmission should begin  as 
described  in 2.4.4.9, below.  This condition is cleared  by  the 
reception of an acknowledgement for the sent frame(s), or by  the 
link being reset.  See 2.4.6.

2.3.5.4.2  Timer T3 Recovery

        Timer  T3 is used to assure the link is still  functional 
during  periods of low information transfer.  Whenever T1 is  not 
running  (no  outstanding I frames), T3 is used  to  periodically 
poll  the  other DXE of a link.  When T3 times out, a RR  or  RNR 
frame  is transmitted as a command and with the P bit  set.   The 
waiting  acknowledgement  procedure  (2.4.4.9,  below)  is   then 
executed.

2.3.5.5  Invalid Frame or FCS Error

        If  an invalid frame is received, or a frame is  received 
with  an FCS error, that frame will be discarded with  no  action 
taken.

2.3.5.6  Frame Rejection Condition

        A  frame  rejection condition occurs  when  an  otherwise 
error-free  frame  has been received with one of  the  conditions 
listed in 2.3.4.3.3 above.

        Once  a  rejection  error occurs, no more  I  frames  are 
accepted  (except for the examination of the P/F bit)  until  the 
error is resolved.  The error condition is reported to the  other 
DXE by sending a FRMR response frame.  See 2.4.5.

2.4  Description of AX.25 Procedures

        The  following  describes the procedures used  to  setup, 
use, and disconnect a balanced link between two DXE stations.

2.4.1  Address Field Operation

2.4.1.1  Address Information

        All   transmitted  frames  shall  have   address   fields 
conforming  to  2.2.13, above.  All frames shall  have  both  the 
destination device and the source device addresses in the address 
field,  with the destination address coming first.   This  allows 
many links to share the same RF channel.  The destination address 
is  always  the address of the station(s) to receive  the  frame, 
while the source address contains the address of the device  that 
sent the frame.
Š        The destination address can be a group name or club  call 
sign if the point-to-multipoint operation is allowed.   Operation 
with  destination addresses other than actual amateur call  signs 
is a subject for further study.

2.4.1.2  Command/Response Procedure

        AX.25  Version 2.0 has implemented  the  command/response 
information   in  the  address  field.   In  order  to   maintain 
compatibility    with   previous   versions   of    AX.25,    the 
command/response information is conveyed using two bits.

        An  upward-compatible AX.25 DXE can determine whether  it 
is  communicating  with  a DXE using an  older  version  of  this 
protocol by testing the command/response bit information  located 
in  bit 7 of the SSID octets of both the destination  and  source 
address subfields.  If both C bits are set to zero, the device is 
using  the  older protocol.  The newer version  of  the  protocol 
always has one of these two bits set to one and the other set  to 
zero, depending on whether the frame is a command or a response.

        The  command/response  information is  encoded  into  the 
address field as shown in Fig. 10.



   Frame Type          Dest. SSID C-Bit    Source SSID C-Bit

  Previous versions             0                    0
  Command (V.2.0)               1                    0
  Response (V.2.0)              0                    1
  Previous versions             1                    1

              Fig. 10 -- Command/Response encoding



        Since  all  frames  are  considered  either  commands  or 
responses, a device shall always have one of the bits set to one, 
and the other bit set to zero.

        The  use  of the command/response  information  in  AX.25 
allows  S frames to be either commands or responses.   This  aids 
maintenance   of  proper  control  over  the  link   during   the 
information transfer state.

2.4.2  P/F Bit Procedures

        The next response frame returned by the DXE to a SABM  or 
DISC command with the P bit set to 1 will be a UA or DM  response 
with the F bit set to 1.  

        The next response frame returned to an I frame with the P 
bit  set  to 1, received during the information  transfer  state, 
will be a RR, RNR, or REJ response with the F bit set to 1.Š
        The next response frame returned to a supervisory command 
frame  with the P bit set to 1, received during  the  information 
transfer state, will be a RR, RNR, or REJ response frame with the 
F bit set to 1.

        The  next  response frame returned to a S  or  I  command 
frame  with  the  P bit set to 1, received  in  the  disconnected 
state, will be a DM response frame with the F bit set to 1.

        The  P  bit  is used in  conjunction  with  the  time-out 
recovery condition discussed in 2.3.5.4, above.

        When not used, the P/F bit is set to zero.

2.4.3  Procedures For Link Set-Up and Disconnection

2.4.3.1  LAPB Link Connection Establishment

        When  one DXE wishes to connect to another DXE,  it  will 
send  a SABM command frame to that device and start  timer  (T1).  
If  the other DXE is there and able to connect, it  will  respond 
with  a UA response frame, and reset both of its  internal  state 
variables  (V(S)  and V(R)).  The reception of  the  UA  response 
frame  at  the  other  end will  cause  the  DXE  requesting  the 
connection  to  cancel the T1 timer and set  its  internal  state 
variables to 0.

        If the other DXE doesn't respond before T1 times out, the 
device requesting the connection will re-send the SABM frame, and 
start  T1  running  again.  The DXE should  continue  to  try  to 
establish  a  connection  until it has  tried  unsuccessfully  N2 
times.  N2 is defined in 2.4.7.2, below.

        If,  upon  reception of a SABM command, the  DXE  decides 
that  it  cannot enter the indicated state, it should send  a  DM 
frame.

        When  receiving a DM response, the DXE sending  the  SABM 
should  cancel  its  T1 timer, and  not  enter  the  information-
transfer state.  

        The  DXE sending a SABM command will ignore  and  discard 
any  frames except SABM, DISC, UA, and DM frames from  the  other 
DXE.

        Frames  other  than UA and DM in response to  a  received 
SABM  will  be  sent  only after the link is set  up  and  if  no 
outstanding SABM exists.

2.4.3.2  Information-Transfer Phase

        After establishing a link connection, the DXE will  enter 
the  information-transfer  state.  In this state,  the  DXE  will 
accept  and  transmit I and S frames according to  the  procedure Šoutlined in 2.4.4, below.

        When  receiving a SABM command while in the  information-
transfer  state,  the  DXE will follow  the  resetting  procedure 
outlined in 2.4.6 below.

2.4.3.3  Link Disconnection

2.4.3.3.1  
     While  in  the information-transfer state,  either  DXE  may 
indicate a request to disconnect the link by transmitting a  DISC 
command frame and starting timer T1 (see 2.4.7).

2.4.3.3.2  
     A DXE, upon receiving a valid DISC command, shall send a  UA 
response  frame  and enter the disconnected state.  A  DXE,  upon 
receiving  a  UA  or DM response to a sent  DISC  command,  shall 
cancel timer T1, and enter the disconnected state.

2.4.3.3.3  
     If  a UA or DM response is not correctly received before  T1 
times out, the DISC frame should be sent again and T1  restarted.  
If  this happens N2 times, the DXE should enter the  disconnected 
state.

2.4.3.4  Disconnected State

2.4.3.4.1  
     A  DXE  in  the disconnected state  shall  monitor  received 
commands  and react upon the reception of a SABM as described  in 
2.4.3.1 above and will transmit a DM frame in response to a  DISC 
command.

2.4.3.4.2  
     In the disconnected state, a DXE may initiate a link  set-up 
as outlined in connection establishment above (2.4.3.1).  It  may 
also  respond  to  the  reception  of  a  SABM  and  establish  a 
connection, or it may ignore the SABM and send a DM instead.

2.4.3.4.3  
     Any  DXE receiving a command frame other than a SABM  or  UI 
frame  with the P bit set to one should respond with a  DM  frame 
with  the  F  bit  set to one.  The  offending  frame  should  be 
ignored.

2.4.3.4.4  
     When  the DXE enters the disconnected state after  an  error 
condition  or if an internal error has resulted in the DXE  being 
in  the  disconnected  state, the DXE  should  indicate  this  by 
sending  a  DM response rather than a DISC frame and  follow  the 
link  disconnection procedure outlined in 2.4.3.3.3, above.   The 
DXE  may then try to re-establish the link using the link  set-up 
procedure outlined in 2.4.3.1, above.

2.4.3.5  Collision RecoveryŠ
2.4.3.5.1  Collisions in a Half-Duplex Environment

        Collisions  of  frames in a half-duplex  environment  are 
taken  care  of  by  the  retry  nature  of  the  T1  timer   and 
retransmission count variable.  No other special action needs  to 
be taken.

2.4.3.5.2  Collisions of Unnumbered Commands

        If sent and received SABM or DISC command frames are  the 
same,  both  DXEs  should  send a UA  response  at  the  earliest 
opportunity, and both devices should enter the indicated state.

        If sent and received SABM or DISC commands are different, 
both  DXEs should enter the disconnected state and transmit a  DM 
frame at the earliest opportunity.

2.4.3.5.3  Collision of a DM with a SABM or DISC

        When  an  unsolicited  DM  response  frame  is  sent,   a 
collision  between it and a SABM or DISC may occur.  In order  to 
prevent  this  DM from being misinterpreted, all  unsolicited  DM 
frames  should  be transmitted with the F bit set to  zero.   All 
SABM  and DISC frames should be sent with the P bit set  to  one.  
This will prevent any confusion when a DM frame is received.

2.4.3.6  Connectionless Operation

        In  Amateur  Radio,  there  is  an  additional  type   of 
operation  that is not feasible using level 2 connections.   This 
operation  is  the  round table, where several  amateurs  may  be 
engaged  in one conversation.  This type of operation  cannot  be 
accommodated by AX.25 link-layer connections.

        The   way   round-table  activity   is   implemented   is 
technically  outside  the AX.25 connection, but still  using  the 
AX.25 frame structure.

        AX.25 uses a special frame for this operation, called the 
Unnumbered  Information (UI) frame.  When this type of  operation 
is  used,  the  destination  address  should  have  a  code  word 
installed  in  it to prevent the users of that  particular  round 
table from seeing all frames going through the shared RF  medium.  
An example of this is if a group of amateurs are in a round-table 
discussion  about  packet  radio, they could put  PACKET  in  the 
destination  address,  so  they would receive  frames  only  from 
others in the same discussion.  An added advantage of the use  of 
AX.25  in this manner is that the source of each frame is in  the 
source  address  subfield,  so  software  could  be  written   to 
automatically display who is making what comments.

        Since  this  mode  is connectionless, there  will  be  no 
requests for retransmissions of bad frames.  Collisions will also 
occur, with the potential of losing the frames that collided.Š
2.4.4  Procedures for Information Transfer

        Once  a  connection  has been  established,  as  outlined 
above, both devices are able to accept I, S, and U frames.

2.4.4.1  Sending I Frames

        Whenever  a DXE has an I frame to transmit, it will  send 
the  I frame with N(S) of the control field equal to its  current 
send  state  variable V(S).  Once the I frame is sent,  the  send 
state  variable  is  incremented  by one.  If  timer  T1  is  not 
running, it should be started.  If timer T1 is running, it should 
be restarted.

        The DXE should not transmit any more I frames if its send 
state variable equals the last received N(R) from the other  side 
of  the link plus seven.  If it were to send more I  frames,  the 
flow control window would be exceed, and errors could result.

        If  a  DXE is in a busy condition, it may  still  send  I 
frames as long as the other device is not also busy.

        If  a  DXE is in the frame-rejection mode, it  will  stop 
sending I frames.

2.4.4.2  Receiving I Frames

2.4.4.2.1  
     If  a DXE receives a valid I frame (one with a  correct  FCS 
and  whose  send sequence number equals  the  receiver's  receive 
state variable) and is not in the busy condition, it will  accept 
the  received I frame, increment its receive state variable,  and 
act in one of the following manners:
        
 1.  If it has an I frame to send, that I frame may be sent with the
     transmitted N(R) equal to its receive state variable V(R) (thus
     acknowledging the received frame).  Alternately, the device may
     send a RR frame with N(R) equal to V(R), and then send the I 
     frame.

 2.  If there are no outstanding I frames, the receiving device will
     send a RR frame with N(R) equal to V(R).  The receiving DXE may
     wait a small period of time before sending the RR frame to be sure
     additional I frames are not being transmitted.

2.4.4.2.2      
     If  the  DXE  is  in a busy condition,  it  may  ignore  any 
received  I  frames without reporting this condition  other  than 
repeating the indication of the busy condition.

        If  a busy condition exists, the DXE receiving  the  busy 
condition   indication  should  poll  the  sender  of  the   busy 
indication periodically until the busy condition disappears.  
Š        A  DXE may poll the busy DXE periodically with RR or  RNR 
frames with the P bit set to one.

        The  reception  of  I  frames  that  contain  zero-length 
information  fields  shall be reported to the next level  but  no 
information field will be transferred.

2.4.4.3  Reception of Out of Sequence Frames

        When  an I frame is received with a correct FCS, but  its 
send sequence number, N(S), does not match the current receiver's 
receive  state  variable, the frame should be discarded.   A  REJ 
frame  shall be sent with a receive sequence number equal to  one 
higher (modulo 8) than the last correctly received I frame if  an 
uncleared  N(S) sequence error condition has not been  previously 
established.   The  received state variable and poll bit  of  the 
discarded  frame should be checked and acted upon, if  necessary, 
before discarding the frame.  

2.4.4.4  Reception of Incorrect Frames

        When  a  DXE receives a frame with an incorrect  FCS,  an 
invalid  frame, or a frame with an improper address,  that  frame 
shall be discarded.

2.4.4.5  Receiving Acknowledgement

        Whenever an I or S frame is correctly received, even in a 
busy condition, the N(R) of the received frame should be  checked 
to  see if it includes an acknowledgement of outstanding  sent  I 
frames.   The T1 timer should be cancelled if the received  frame 
actually  acknowledges previously unacknowledged frames.  If  the 
T1  timer is cancelled and there are still some frames that  have 
been sent that are not acknowledged, T1 should be started  again.  
If  the T1 timer runs out before an acknowledgement is  received, 
the  device  should proceed to the  retransmission  procedure  in 
2.4.4.9.

2.4.4.6  Receiving Reject

        Upon receiving a REJ frame, the transmitting DXE will set 
its  send  state variable to the same value as  the  REJ  frame's 
received sequence number in the control field.  The DXE will then 
retransmit  any  I  frame(s) outstanding at  the  next  available 
opportunity conforming to the following:

 1.  If the DXE is not transmitting at the time, and the  channel 
     is  open,  the  device  may commence  to  retransmit  the  I 
     frame(s) immediately.

 2.  If   the   DXE  is  operating  on  a   full-duplex   channel 
     transmitting  a UI or S frame when it receives a REJ  frame, 
     it may finish sending the UI or S frame and then  retransmit 
     the I frame(s).
Š 3.  If   the   DXE  is  operating  in  a   full-duplex   channel 
     transmitting  another I frame when it receives a REJ  frame, 
     it  may  abort  the  I  frame  it  was  sending  and   start 
     retransmission of the requested I frames immediately.

 4.  The DXE may send just the one I frame outstanding, or it may 
     send  more than the one indicated if more I frames  followed 
     the  first  one not acknowledged, provided the total  to  be 
     sent does not exceed the flow-control window (7 frames).

        If the DXE receives a REJ frame with the poll bit set, it 
should  respond with either a RR or RNR frame with the final  bit 
set before retransmitting the outstanding I frame(s).

2.4.4.7  Receiving a RNR Frame

        Whenever  a  DXE  receives a RNR  frame,  it  shall  stop 
transmission  of  I  frames until the  busy  condition  has  been 
cleared.   If timer T1 runs out after the RNR was  received,  the 
waiting  acknowledgement  procedure  listed  in  2.4.4.9,  below, 
should  be  performed.  The poll bit may be used  in  conjunction 
with  S  frames  to test for a change in  the  condition  of  the 
busied-out DXE.

2.4.4.8  Sending a Busy Indication

        Whenever a DXE enters a busy condition, it will  indicate 
this  by sending a RNR response at the next  opportunity.   While 
the  DXE is in the busy condition, it may receive and  process  S 
frames,  and if a received S frame has the P bit set to one,  the 
DXE should send a RNR frame with the F bit set to one at the next 
possible  opportunity.   To  clear the busy  condition,  the  DXE 
should  send either a RR or REJ frame with the received  sequence 
number equal to the current receive state variable, depending  on 
whether the last received I frame was properly received or not.

2.4.4.9  Waiting Acknowledgement

        If timer T1 runs out waiting the acknowledgement from the 
other DXE for an I frame transmitted, the DXE will restart  timer 
T1  and transmit an appropriate supervisory command frame (RR  or 
RNR)  with  the  P  bit set.  If the  DXE  receives  correctly  a 
supervisory  response frame with the F bit set and with  an  N(R) 
within  the  range from the last N(R) received to the  last  N(S) 
sent  plus  one, the DXE will restart timer T1 and will  set  its 
send  state  variable  V(S) to the received N(R).   It  may  then 
resume   with   I  frame  transmission  or   retransmission,   as 
appropriate.  If, on the other hand, the DXE receives correctly a 
supervisory response frame with the F bit not set, or an I  frame 
or  supervisory command frame, and with an N(R) within the  range 
from  the last N(R) received to the last N(S) sent plus one,  the 
DXE will not restart timer T1, but will use the received N(R)  as 
an  indication of acknowledgement of transmitted I frames  up  to 
and including I frame numbered N(R)-1.
Š        If timer T1 runs out before a supervisory response  frame 
with  the  F  bit set is received, the  DXE  will  retransmit  an 
appropriate supervisory command frame (RR or RNR) with the P  bit 
set.  After N2 attempts to get a supervisory response frame  with 
the  F bit set from the other DXE, the DXE will initiate  a  link 
resetting procedure as described in 2.4.6, below.

2.4.5  Frame Rejection Conditions

        A  DXE  shall initiate the frame-reset procedure  when  a 
frame  is received with the correct FCS and address field  during 
the information-transfer state with one or more of the conditions 
in 2.3.4.3.3, above.

        Under these conditions, the DXE will ask the other DXE to 
reset  the  link by transmitting a FRMR response as  outlined  in 
2.4.6.3, below.

        After sending the FRMR frame, the sending DXE will  enter 
the  frame reject condition.  This condition is cleared when  the 
DXE that sent the FRMR frame receives a SABM or DISC command,  or 
a DM response frame.  Any other command received while the DXE is 
in the frame reject state will cause another FRMR to be sent  out 
with the same information field as originally sent.

        In  the  frame rejection condition, additional  I  frames 
will not be transmitted, and received I frames and S frames  will 
be discarded by the DXE.

        The DXE that sent the FRMR frame shall start the T1 timer 
when  the  FRMR is sent.  If no SABM or DISC  frame  is  received 
before the timer runs out, the FRMR frame shall be retransmitted, 
and   the  T1  timer  restarted  as  described  in  the   waiting 
acknowledgement section (2.4.4.9) above.  If the FRMR is sent  N2 
times without success, the link shall be reset.

2.4.6  Resetting Procedure

2.4.6.1  
     The   resetting  procedure  is  used  to   initialize   both 
directions  of  data  flow  after  a  nonrecoverable  error   has 
occurred.   This resetting procedure is used in the  information-
transfer state of an AX.25 link only.

2.4.6.2  
     A DXE shall initiate a reset procedure whenever it  receives 
an unexpected UA response frame or an unsolicited response  frame 
with  the  F bit set to one.  A DXE may also initiate  the  reset 
procedure  upon receipt of a FRMR frame.  Alternatively, the  DXE 
may  respond to a FRMR by terminating the connection with a  DISC 
frame.

2.4.6.3  
     A  DXE  shall  reset the link by sending a  SABM  frame  and 
starting  timer  T1.  Upon receiving a SABM frame  from  the  DXE Špreviously connected to, the receiver of a SABM frame should send 
a  UA  frame back at the earliest opportunity, set its  send  and 
receive  state  variables,  V(S) and V(R), to zero  and  stop  T1 
unless it has sent a SABM or DISC itself.  If the UA is correctly 
received by the initial DXE, it resets its send and receive state 
variables, V(S) and V(R), and stops timer T1.  Any busy condition 
that previously existed will also be cleared.

        If  a  DM response is received, the DXE  will  enter  the 
disconnected  state  and  stop timer T1.  If timer  T1  runs  out 
before  a UA or DM response frame is received, the SABM  will  be 
retransmitted  and timer T1 restarted.  If timer T1 runs  out  N2 
times,  the  DXE  will  enter the  disconnected  state,  and  any 
previously existing link conditions will be cleared.

     Other  commands  or  responses received by  the  DXE  before 
completion of the reset procedure will be discarded.

2.4.6.4  
     One  DXE  may request that the other DXE reset the  link  by 
sending  a  DM response frame.  After the DM frame is  sent,  the 
sending DXE will then enter the disconnected state.

2.4.7  List of System Defined Parameters

2.4.7.1  Timers

        To   maintain  the  integrity  of  the  AX.25   level   2 
connection, use of these timers is recommended.

2.4.7.1.1  Acknowledgement Timer T1

        The  first timer, T1, is used to make sure a DXE  doesn't 
wait  forever  for a response to a frame it  sends.   This  timer 
cannot be expressed in absolute time, since the time required  to 
send frames varies greatly with the signaling rate used at  level 
1.   T1  should take at least twice the amount of time  it  would 
take  to send maximum length frame to the other DXE, and get  the 
proper response frame back from the other DXE.  This would  allow 
time for the other DXE to do some processing before responding.

        If  level  2 repeaters are to be used, the  value  of  T1 
should be adjusted according to the number of repeaters the frame 
is being transferred through.

2.4.7.1.2  Response Delay Timer T2

        The  second timer, T2, may be implemented by the  DXE  to 
specify  a maximum amount of delay to be introduced  between  the 
time an I frame is received, and the time the resulting  response 
frame is sent.  This delay may be introduced to allow a receiving 
DXE to wait a short period of time to determine if there is  more 
than  one frame being sent to it.  If more frames  are  received, 
the  DXE can acknowledge them at once (up to seven), rather  than 
acknowledge  each individual frame.  The use of timer T2  is  not Šmandatory,  but  is recommended to  improve  channel  efficiency.  
Note  that, on full-duplex channels, acknowledgements should  not 
be delayed beyond k/2 frames to achieve maximum throughput.   The 
k parameter is defined in 2.4.7.4, below.

2.4.7.1.3  Inactive Link Timer T3

        The third timer, T3, is used whenever T1 isn't running to 
maintain  link integrity.  It is recommended that whenever  there 
are  no  outstanding  unacknowledged I  frames  or  P-bit  frames 
(during  the information-transfer state), a RR or RNR frame  with 
the  P  bit set to one be sent every T3 time units to  query  the 
status  of the other DXE.  The period of T3 is  locally  defined, 
and  depends greatly on level 1 operation.  T3 should be  greater 
than T1, and may be very large on channels of high integrity.

2.4.7.2  Maximum Number of Retries (N2)

        The maximum number of retries is used in conjunction with 
the T1 timer.

2.4.7.3  Maximum Number of Octets in an I Field (N1)

        The maximum number of octets allowed in the I field  will 
be 256.  There shall also be an integral number of octets.

2.4.7.4  Maximum Number of I Frames Outstanding (k)

        The  maximum number of outstanding I frames at a time  is 
seven.

                              END.
--------------------------------------------------------------------------