Transporting Version 7 of Icon*


                        Ralph E. Griswold





                             TR 88-9

























                        January 29, 1988


                 Department of Computer Science

                    The University of Arizona

                      Tucson, Arizona 85721




*This work was supported by the National Science Foundation under
Grant DCR-8502015.













                 Transporting Version 7 of Icon




1.  Background

   The implementation of the Icon programming language is large
and complex [1]. It is, however, written almost entirely in C,
and it is designed to be portable to a wide range of computers
and operating systems.

   The implementation was developed on a UNIX* system.  It has
been installed on a wide range of UNIX systems, from mainframes
to personal computers. Putting Icon on a new UNIX system is more
a matter of installation than porting [2].  There presently also
are installations of Icon for VAX/VMS, the Amiga, the Atari ST,
the Macintosh under MPW, and MS-DOS. This document addresses the
problems and procedures for porting Icon to other operating sys-
tems and computers.

   The current version of Icon is Version 7 [3].  All installa-
tions of Version 7 of Icon are obtained from common source code,
using conditional compilation to select system-dependent code.
Consequently, transporting Icon to a new system is largely a
matter of selecting appropriate values for configuration parame-
ters, deciding among alternative definitions, and possibly adding
some code that is computer- or operating-system-dependent.

   A small amount of assembly-language code is needed for a com-
plete installation.  See Section 7. This code is optional and
only affects co-expressions and checking for arithmetic overflow.
A running version of the language can be obtained by working only
in C.

   Transporting Icon to a new system is a fairly complex task,
although there are many aids to simplify mechanical tasks. Read
this report carefully before beginning a port.  Understanding the
Icon programming language is helpful during the debugging phase
of a port. See [3-5]


2.  Requirements

C Data Sizes

   Icon places the following requirements on C data sizes:

                          
*UNIX is a trademark of AT&T Bell Laboratories.




                             - 1 -








     +   chars must be 8 bits.

     +   ints must be 16, 32, or 64 bits.

     +   longs and pointers must be 32 or 64 bits.

     +   All pointers must be the same length.

     +   longs and pointers must be the same length.

If your C data sizes do not meet these requirements, do not
attempt to transport Icon. Call the Icon Project for advice.
Note: Icon has not yet been ported to a computer with 64-bit C
data sizes; such a port may encounter problems.

The C Compiler

   The main requirement for implementing Icon is a production-
quality C compiler that supports at least the de facto ``K&R''
standard [6].  The term ``production quality'' implies robust-
ness, correctness, the ability to handle large files and compli-
cated expressions, and a comprehensive run-time library.

   C preprocessor should conform either to the ANSI C standard
[7] or to the de facto standard for UNIX C preprocessors.  In
particular, Icon uses the C preprocessor to concatenate strings
and substitute arguments within quotation marks. For the ANSI
standard, the following definitions are used:

        #define Cat(x,y) x##y
        #define Lit(x) #x

For the UNIX de facto standard, the following definitions are
used:

        #define Ident(x) x
        #define Cat(x,y) Ident(x)y
        #define Lit(x) "x"

The following program can be used to test these preprocessor
facilities:

        Cat(ma,in)()
        {
           printf(Lit(Hello world\n));
        }

If this program does not compile and print Hello world using one
of the sets of definitions above, there is no point in proceed-
ing.  Contact the Icon Project as described in Section 8 for
alternative approaches.






                             - 2 -








Memory

   The Icon programming language requires a substantial amount of
memory.  The practical minimum is 512kb.

File Space

   The source code for Icon is large - about 850kb.  Compilation
and testing require considerably more space.  While the implemen-
tation can be divided into components that can be transported
separately, this approach may be painful.


3.  Organization of the Implementation

   Icon was developed on a hierarchical file system. To facili-
tate file transfer between different operating systems and to
simplify porting to systems that do not support file hierarchies,
the source code for Icon is provided both in hierarchical form
and in a ``flat'' form in which all files reside in the same
area.  This document applies to both the hierarchical and flat
forms. Some of the supplementary documentation on Icon refers to
file hierarchies. In interpreting this documentation on flat sys-
tems, simply ignore the directories in path specifications; the
file names themselves are the same in the hierarchical and flat
version.

3.1  Source Code

   There are four components of Icon:

     itran   a translator that converts source-language programs
             to ucode, an assembly language for an abstract
             ``Icon machine''.

     ilink   a linker that combines one or more ucode files into
             a single binary icode file in executable format for
             the Icon machine.

     iconx   an executor for icode, including a run-time system
             that supports the operations of the Icon language.

     icont   a command processor that provides a user interface
             for running itran, ilink, and iconx.

itran

   The translator is relatively straightforward. It contains a
lexical analyzer, a parser, a code generator, and support rou-
tines. The translator is independent of the architecture of the
computer on which it runs and its ucode output consists of print-
able text.





                             - 3 -








ilink

   The linker is somewhat more complex than the translator. It
reads ucode files and outputs binary code and data structures
that are needed during execution. Because these data structures
depend to some extent on the architecture of the computer on
which Icon runs, the linker contains some machine-dependent
parameters.

iconx

   The executor is the largest and most complex of the components
of Icon. Its data structures depend on the architecture of the
computer on which Icon runs, and it includes code for all the
operations in the Icon language. In addition, it manages storage
dynamically.

icont

   The command processor is a small program that executes the
other components of Icon. Its main function is to analyze the
user's command line and take appropriate actions.  The command
processor is a convenience, not a necessity.  A command-language
script can be used in its place.

   The files related to the source are packaged in five groups:

        itran        files for itran
        ilink        files for ilink
        iconx        files for iconx
        icont        files for icont
        h            header files

The header files are in a separate package, since some are used
in several components of Icon. In some forms of the distribution,
iconx comes in two parts, since it is is too large to fit on a
single diskette.

   Appendix A lists the files of each component of Icon. Some
header files are used in several components; these are identified
in the appendix.  The files itran.bat, ilink.bat, iconx.bat, and
icont.bat are scripts that indicate what files are to be compiled
and loaded to produce the respective components. These scripts
were derived from a UNIX implementation, but they can be adapted
easily to other systems.

3.2  Tests

   Test programs are divided into two parts. The first part,
referred to as suite1, contains test programs and the expected
output for itran and ilink. The second part, referred to as
suite2, contains test programs and expected output for iconx.

   See Section 6 for more information about the test programs.



                             - 4 -








4.  An Overview of the Porting Process

   The first step in the porting process is to configure the
source code for the new system. This process is described in Sec-
tion 5.1. After this is done, the components need to be ported,
one by one.

   The porting process for each component of Icon is essentially
the same:

     +  provide code and definitions that are system-dependent

     +  compile the source files and link them to produce execut-
        able binary files

     +  test the result

     +  debug, iterating over the previous steps as necessary

   The components should be ported in the order given above:
itran, ilink, iconx, and icont. Of course, bugs in previously
ported components may not show up until subsequent components are
tested.

   In addition to this obvious sequence of steps, some aspects of
the implementation may be deferred until the entire system is
running, or they may be implemented in a preliminary manner and
subsequently refined. For example, the assembly-language portions
of Icon are best left unimplemented until the rest of the system
is running. Considerable frustration can be avoided if problems
that come up can be circumvented with temporary expedients until
the majority of the implementation is working properly. Simi-
larly, conservative choices should be made during the initial
phases of the implementation.


5.  Conditional Compilation

   Conditional compilation is used extensively in Icon to select
code that is appropriate to a particular installation. Conceptu-
ally, conditional compilation can be divided into two categories:

     (1)  Matters related to the details of computer architec-
          ture, run-time system idiosyncrasies, specific C com-
          pilers, and operating-system variants.

     (2)  Matters that are specific to operating systems that are
          distinctly different, such as MS-DOS, UNIX, and VMS.

5.1  Parameters and Definitions

   There are many constants in the source code for Icon that vary
from system to system. Default values are provided so that the
usual cases are handled automatically.  The file define.h



                             - 5 -








contains C preprocessor definitions for parameters that differ
from the defaults or that must be provided on an individual
basis. This file initially contains values for a ``vanilla'' 32-
bit system.  If your system closely approximates a ``vanilla''
system, you will have few changes to make to define.h. Over the
range of possible systems, there are many possibilities as
described below.

   The definitions are grouped into categories so that any neces-
sary changes to define.h can be approached in a logical way.

C preprocessor: Icon preprocessor directives use string concate-
nation and substitution of arguments within quotation marks as
described in Section 2. By default, the original UNIX method of
accomplishing this is used.  A different method is specified in
the C draft standard [6]. If your C compiler supports the draft
standard, add

        #define Standard

to define.h.

C sizing and alignment: There are four constants that relate to
the size of C data and alignment:

        IntBits     (default: 32)
        WordBits    (default: 32)
        Double      (default: undefined)

IntBits is the number of bits in a C int. It may be 16, 32, or
64. WordBits is the number of bits in a C long and pointer
(Icon's ``word''). It may be 32 or 64.  If your C library expects
doubles to be aligned at double-word boundaries, add

        #define Double

to define.h.

Floating-point arithmetic: There are four optional definitions
related to floating-point arithmetic:

        Big         (default: 9007199254740092.)
        LogHuge     (default: 309)
        Precision   (default: 10)
        ZeroDivide  (default: undefined)

The values of Big, LogHuge, and Precision give, respectively, the
largest floating-point number that does not loose precision, the
maximum base-10 exponent + 1 of a floating-point number, and the
number of digits provided in the string representation of a
floating-point number. If the default values given above do not
suit the floating-point arithmetic on your system, add appropri-
ate definitions to define.h. If your system needs a software
check for division by floating-point zero, add



                             - 6 -








        #define ZeroDivide

to  define.h.

Include file location: The location of the include file time.h
varies from system to system. Its default location is <time.h>.
If it resides at a different location on your system (usually
<sys/time.h>), add an appropriate definition of SysTime to
define.h, as in

        #define SysTime <sys/time.h>

If the location is incorrect, a fatal error will occur during the
compilation of src/iconx/lmisc.c.  The use of this definition
also depends on your C preprocessor making macro substitutions in
#include directives. Most preprocessors do, but if yours does
not, edit src/iconx/lmisc.c and replace SysTime there by the
appropriate value. If you have to do this, make a note to come
back later and place the definition under the control of condi-
tional compilation.

Run-time routines: The support for some run-time routines varies
from system to system.  The related constants are:

        Fork        (default: fork)
        IconGcvt    (default: undefined)
        IconQsort   (default: undefined)
        NoAtof      (default: undefined)
        SysMem      (default: undefined)
        index       (default: undefined)
        rindex      (default: undefined)

If your system supports vfork(2), add

        #define Fork vfork

to define.h. This definition is used only in icont.c.

If IconGcvt and IconQsort are defined, versions of gcvt(3) and
qsort(3) in the Icon system are used in place of the routines
normally provided in the C run-time system. These constants only
need to be defined if the versions of these routines in your
run-time system are defective or missing.

The C run-time routine atof(3) normally is used in the Icon
linker to convert strings for real literals to corresponding
floating-point numbers.  If the version of atof on your system
does not work properly, add

        #define NoAtof

to define.h.  This replaces the use of atof by in-line conversion
code.




                             - 7 -








If your run-time system includes memcpy(3) and memset(3), add

        #define SysMem

to define.h.  Otherwise, versions of these routines in the Icon
system are used.

Different run-time systems use different names for the routines
for locating substrings within strings. The source code for Icon
uses index and rindex. The other possibilities are strchr and
strrchr. If your system uses the latter names, add

        #define index strchr
        #define rindex strrchr

to define.h.

Host identification: The identification of the host computer as
given by the Icon keyword &host needs to be specified in
define.h.  The definition

        #define HostStr "unknown host"

is provided in define.h initially.  This definition should be
changed to an appropriate value for your system.

Storage management: Storage management is one of the most complex
components of Icon and the one that is most likely to cause prob-
lems in porting. There are two alternative forms of memory
management: fixed-regions and expandable-regions.  In fixed-
regions memory management, Icon's storage regions are allocated
at the beginning of execution and do not increase in size. If
they are not large enough, program execution terminates with an
error if more space is needed. In expandable-regions memory
management, Icon's storage regions also are allocation at the
beginning of execution, but it they are not big enough, they are
increased using sbrk.

Many systems do not support sbrk, so the fixed-regions form of
memory management is necessary, although it is more limiting.
This form of memory management is recommended for an initial
port, even if sbrk is supported. If the port is otherwise suc-
cessful, expandable-regions management can be attempted later.

Initially, define.h contains

        #define FixedRegions

which enables fixed-regions management. Remove this definition if
you want expandable-regions management.

Icon includes its own versions of malloc, calloc, realloc, and
free so that it can manage its storage regions without interfer-
ence from allocation by the operating system. Normally, Icon's



                             - 8 -








versions of these routines are loaded instead of the system
library routines.  Leave things are they are in the initial con-
figuration, but if your system insists on loading its own library
routines, multiple definitions will occur as a result of the ld
in src/iconx.  If multiple definitions occur, go back and add

        #define IconAlloc

to define.h. This definition causes Icon's routines to be named
differently to avoid collision with the system routine names.

One possible effect of this definition is to interfere with
Icon's expansion of its memory region in expandable-regions
memory management.

Environment variables: If your system does not support environ-
ment variables (via the run-time library routine getenv), add the
following line to define.h:

        #define NoEnvVars

This disables Icon's ability to change internal parameters to
accommodate special user needs (such as using memory region sizes
different from the defaults), but does not otherwise interfere
with the use of Icon.

Character set:

The implementation of Icon was designed on the assumption it
would run on computers using the ASCII character set. Some work
has been done toward supporting the EBCDIC character set as an
alternative. If you are porting Icon to a computer that uses the
EBCDIC character set, add

        #define EBCDIC

to define.h.

Support for the EBCDIC character set is not yet complete and some
places in the source code need modification for it.  Examine code
under #ifdef EBCDIC in fstr.c, fstranl.c, imain.c, lex.c,
rconv.c, and toktab.c.

There also is an option that allows alternative representations
of some characters commonly used in Icon programs that are not
supported by many EBCDIC terminals and printers. The standard
characters and their alternative forms are:

        standard  alternative
          {         $(
          }         $)
          [         $<
          ]         $>




                             - 9 -








To enable this option, add

        #define ExtChars

to define.h.

Miscellaneous: There are two other definitions that may be needed
in some cases:

        Hz          (default: 60)
        UpStack     (default: undefined)

If you are running in a 50-hz environment, add

        #define Hz 50

to define.h.

Most computers have downward-growing C stacks, for which stack
addresses decrease as values are pushed. If you have an upward-
growing stack, for which stack addresses increase as values are
pushed, add

        #define UpStack

to define.h.

Optional features: The implementation of co-expressions and
arithmetic overflow checking require assembly language routines.
Initially, define.h contains

        #define NoCoexpr
        #define NoOver

These definitions disable co-expressions and arithmetic overflow
checks.  Leave these definitions in for the first round, although
you may want to remove them later and implement these features
(see Section 7).

5.2  Operating System Differences

   Conditional compilation for operating systems usually is due
to differences in run-time library routines, differences in file
naming, the handling of input and output, and environmental fac-
tors.

   The presently supported operating system are AmigaDos, Atari
ST TOS, the Macintosh under MPW, MS-DOS, UNIX, and VAX/VMS.
There hooks for transporting to MVS and VM and for an unspecified
system (a new port).  The associated defined symbols are







                             - 10 -








        AMIGA       AmigaDos
        ATARI ST    Atari ST TOS
        MACINTOSH   Macintosh
        MSDOS       MS-DOS
        MVS         MVS
        PORT        new port
        UNIX        UNIX
        VM          VM
        VMS         VMS

Conditional compilation uses logical expressions composed from
these symbols.  An example is:

                .
                .
                .
        #if MSDOS
                .
                .       /* code for MS-DOS */
                .
        #endif

        #if UNIX || VMS
                .
                .       /* code for UNIX and VMS */
                .
        #endif
                .
                .
                .

Each symbol must be defined to be either 1 (for the target
operating system) or 0 (for all other operating systems).  This
is accomplished by defining the symbol for the target operating
system to be 1 in define.h. In config.h, which includes define.h,
all other operating-system symbols are automatically defined to
be 0.

   Logical conditionals with #if are used instead of defined or
undefined names with #ifdef to avoid nested conditionals, which
become very complicated and difficult to understand when there
are several alternative operating systems.  Note that it is
important not to use #ifdef accidentally in place of #if, since
all the names are defined.

   The file define.h initially contains

        #define PORT

It you are porting to MVS or VM, change the symbol accordingly.
Otherwise, leave it as is; later you should come back and change
PORT to some more appropriate name.

   To make it easy to locate all the places where there is code



                             - 11 -








that may be dependent on the operating system, such code is
bracketed by unique comments of the following form:

        /*
         * The following code is operating-system dependent.
         */
                       .
                       .
                       .
        /*
         * End of operating-system specific code.
         */

Between these beginning and ending comments, the code for dif-
ferent operating systems is provided using conditional expres-
sions such as those indicated above.

   There presently are a total of 76 segments that contain such
code.  The files that contain operating-system-dependent code are
listed in Appendix B.  Look through some of the files that con-
tain such segments to get an idea of what is involved.  Each seg-
ment contains comments that describe the purpose of the code.  In
most cases, the most likely code or a suggestion is given in the
conditional code under PORT.  In some cases, no code will be
needed. In others, code for an existing system may suffice for
the new system.

   In any event, code for the new operating system name must be
added to each such segment, either by adding it to a logical dis-
junction, as in

        #if MSDOS || UNIX || PORT
             .
             .
             .
        #endif

        #if VMS
             .
             .
             .
        #endif

or by filling in the segment with the appropriate code, as in

        #if PORT
                .
                .       /* code for the the port */
                .
        #endif

If no code for the target operating system, a comment should be
added so that it is clear that the situation has been considered.




                             - 12 -








   You may find need for code that is operating-system dependent
at a place where no such dependency presently exists.  If this
happens, add a new segment similar to the other ones, being sure
to provide something appropriate for all operating systems.  Do
not simply add code like

        #if PORT
             .
             .
             .
        #endif

without empty code for the other systems, since this will inter-
fere with transportation to other systems in the future.

   Do not use #else constructions; this encourages errors and
obscures the mutually exclusive nature of operating system
differences.


6.  Building and Testing

6.1  The Translator

   Start by compiling all the C programs listed in tran.bat.
Load the resulting object files to produce itran. With any luck,
this will go without problems, since itran is largely machine-
independent. If you encounter problems, check the portions of
code containing operating system dependencies.

   Once you have a version of itran, try it on the Icon programs
in suite1. For example, to translate bitops.icn in suite1, do

        itran bitops.icn

This should yield two ucode files, bitops.u1 and bitops.u2.  The
.u1 file contains procedure declarations and code for the Icon
machine; the .u2 file contains global declaration information.

   These files both consist of printable text.  They should be
identical to the corresponding files in suite1. Be careful to run
itran in a way that does not overwrite the ucode files in suite1.

   More than likely, if you get any ucode files at all, they will
be correct, since the translator is machine-independent and port-
able and no significant problems have been encountered with it in
other ports.

6.2  The Linker

   Compile all the C files listed in ilink.bat and load them to
get ilink.  You may encounter more problems here, since the
linker is somewhat dependent on the sizes of C data objects and
does more sophisticated input and output than the translator.



                             - 13 -








   Once you have ilink, test it on ucode files as follows:

        ilink -L bitops.u1

Only the .u1 file is named for the linker, but both the .u1 and
.u2 files must be present for ilink. The -L option causes ilink
to produce a debugging output file with the suffix .ux - in this
case, bitops.ux. Compare this file to the corresponding one in
suite1. The two files may not be exactly the same, since the
debugging output depends on C sizes (the distributed files are
for 32-bit ints) and idiosyncrasies of fprintf. However, the
files should be similar. Do not worry about small differences.

6.3  The Run-Time System

   If you get this far without apparent problems, you are ready
for the next - and most difficult - part of the transporting pro-
cess: iconx.  Compile all the C programs listed in iconx.bat and
load them to form iconx.

   As a first test, try iconx on hello.icn in suite1 as follows:

        itran hello.icn
        ilink hello.u1
        iconx hello

If all is well, the last step should print out "hello world" and
some identifying information.

   Once this test has been passed, more rigorous testing should
follow.  At this point, you probably will want to devise a way of
testing programs, since there are a large number of tests. This
is done for the MS-DOS implementation using the following .bat
file:























                             - 14 -








        echo off
        itran -s %1.icn
        ilink %1.u1
        echo Executing
        if not exist %1.dat goto skip1
        iconx  %1 <%1.dat >%1.out
        goto comp
        :skip1
        iconx -e - %1 >%1.out
        :comp
        compare %1.out stand\%1.out -t -w -l %1.dif
        type %1.dif
        del %1
        del %1.u1
        del %1.u2
        erase local\%1.out
        erase local\%1.dif
        movefile %1.out local
        movefile %1.dif local
        echo on

On UNIX systems, the following script is used to test all the
files in a list:

        for i in `cat $1.lst`
        do
           rm -f local/$i.out
           echo Running $i
           itran $i.icn
           ilink $i.u1
           if test -r $i.dat
           then
              iconx $i <$i.dat >local/$i.out 2>&1
           else
              iconx $i >local/$i.out 2>&1
           fi
           echo Checking $i
           diff local/$i.out stand/$i.out
           rm -f $i
        done

While these methods are adapted to specific operating-system
capabilities, something similar can be concocted for other sys-
tems. Making such a facility as easy to use as possible is worth
the effort.

   In suite2 there many Icon programs for testing different
aspects of iconx. These range from simple tests to ``grinders''.
The names of the test programs are listed in the following files:








                             - 15 -








        icon.lst  short programs*
        expr.lst  programs that contain a wide variety of expressions
        check.lst programs that may produce different results on different systems
        extra.lst programs that test additional features
        work.lst  long-running programs*
        version7.lstprograms that test new features in Version 7*

The lists flagged with a * contains tests that require data files
that are included in suite2 with the ending .dat. For example,
the Icon program meander.icn, listed in icon.lst, takes data from
meander.dat.  suite2 also contains files whose names end in .out
that contain the expected output of each test program.  For exam-
ple, the expected output of meander.icn is contained in
meander.out.

   The programs listed in icon.lst should produce output identi-
cal to that in their corresponding .out files. Any discrepancies
should be checked carefully and corrections made before continu-
ing.

   The programs listed in expr.lst execute a wide variety of
individual expressions. Ideally, there should be no discrepancies
between their output and the expected output. If there are many
discrepancies, something serious probably is wrong. If there are
only a few discrepancies, they may be noted while other testing
is conducted.

   The programs listed in check.lst certainly will show some
differences, since they test features whose results are time- and
environment-dependent. Other differences may show up also.  These
do not necessarily indicate problems. For examples, minor differ-
ences in the results of floating-point arithmetic are common in
these tests.

   The programs listed in extra.lst test some features that are
not tested elsewhere. They should be treated like the programs
listed in icon.lst.

   In work.lst are listed several programs that run for a very
long time and exercise some parts of the implementation exten-
sively.

   Since storage management is one of the parts of Icon that is
likely to give trouble, there are special storage-management
tests in gc.lst.  These programs run for a long period of time.
One program may show a difference in output if the fixed-regions
version of memory management is used, since it may run out of
space.

   Not much general advice can be given about locating and
correcting problems that may show up in testing iconx. It has to
be done the hard way and may involve learning more about the Icon
language [4] and how it is implemented [1].  A good debugger can
be very helpful.



                             - 16 -








6.4  The Command Processor

   See the remarks about icont in Section 3.1. If icont is to be
implemented, compile icont.c and load it to form icont.

   Test icont on hello.icn in suite1 as follows:

        icont hello.icn -x

If all is well, hello.icn should be translated, linked, and exe-
cuted to produce the output given in the preceding section.

   icont supports several options. See [8] for a complete list.
Various combinations of options should be tested to confirm that
icont is working properly.


7.  Assembly-Language Code

   Once Icon is running satisfactorily, you may wish to implement
the features that require assembly language: co-expressions and
arithmetic overflow checking.

7.1  Co-Expressions

   Note: If your system does not allow the C stack to be at an
arbitrary place in memory, there is probably little hope of
implementing co-expressions.  If you do not implement co-
expressions, the only effect will be that Icon programs that
attempt to use a co-expression will terminate with an error mes-
sage.

   All aspects of co-expression creation and activation are writ-
ten in C in Version 7 except for a routine, coswitch, that is
needed for context switching. This routine requires assembly
language, since it must manipulate hardware registers.  It either
can be written as a C routine with asm directives or as an assem-
bly language routine.

   Calls to the context switch have the form
coswitch(old cs,new cs,first), where old cs is a pointer to an
array of words that contain C state information for the current
co-expression, new cs is a pointer to an array of words that hold
C state information for a co-expression to be activated, and
first is 1 or 0, depending on whether or not the new co-
expression has or has not been activated before.  The zeroth ele-
ment of a C state array always contains the hardware stack
pointer (sp) for that co-expression. The other elements can be
used to save any C frame pointers and any other registers your C
compiler expects to be preserved across calls.

   The default number of elements for saving the C state is 15.
This number may be changed by adding




                             - 17 -








        #define CStateSize n

to define.h, where n is the number of elements needed.

   The first thing coswitch does is to save the current pointers
and registers in the old cs array. Then it tests first.  If first
is zero, coswitch sets sp from new cs[0], clears the C frame
pointers, and calls interp. If first is not zero, it loads the
(previously saved) sp, C frame pointers, and registers from
new cs and returns.

   Written in C, coswitch has the form:

        /*
         * coswitch
         */
        coswitch(old cs, new cs, first)
        int *old cs, *new cs;
        int first;
        {
                            .
                            .
                            .
                    /* save sp, frame pointers, and other registers in old cs */
                            .
                            .
                            .
           if (first == 0) {/* this is first activation */
                            .
                            .
                            .
                    /* load sp from new cs[0] and clear frame pointers */
                            .
                            .
                            .
              interp(0, 0);
              syserr("interp() returned in coswitch");
              }
           else {
                            .
                            .
                            .
                    /* load sp, frame pointers, and other registers from new cs */
                            .
                            .
                            .
              }
        }


   After you implement rswitch, remove the #define NoCoexpr from
define.h.

   To test your context switch, run the programs in coexpr.lst.



                             - 18 -








Ideally, there should be no differences in the comparison of out-
puts.

   If you have trouble with your context switch, the first thing
to do is double-check the registers that your C compiler expects
to be preserved across calls - different C compilers on the same
computer may have different requirements.

   Another possible source of problems is built-in stack check-
ing.  Co-expressions rely on being able to specify an arbitrary
region of memory for the C stack. If your C compiler generates
code for stack probes that expects the C stack to be at a
specific location, you may need to disable this code or replace
it with something more appropriate.

7.2  Overflow Checking

   C does not provide overflow checking for integer addition,
subtraction, or multiplication. Icon, on the other hand, is sup-
posed to check for overflow. This usually requires assembly-
language code.

   Initially, define.h contains the definition

        #define NoOver

which causes overflow checking to be bypassed.

   If you do not want to implement overflow checking, you need do
nothing.  The only effect will be that overflow will not be
detected.

   If you want to implement overflow checking, remove the defini-
tion of NoOver from your define.h and write routines ckadd,
cksub, and ckmul that call fatalerr(-203,0) in the case of over-
flow.

   Note: It often is harder to test for overflow for multiplica-
tion than for addition and subtraction. A dummy routine that sim-
ply returns can be provided for multiplication if this is the
case on your system.


   To test overflow checking, run the programs in over.lst.
There should be no differences in the comparison of outputs if
overflow checking is working properly.

   You should also rerun previous tests at this point to make
sure that arithmetic still works properly.








                             - 19 -








8.  Trouble Reports and Feedback

   If you run into problems, contact us at the Icon Project:

        Icon Project
        Department of Computer Science
        Gould-Simpson Science Building
        The University of Arizona
        Tucson, AZ   85721
        U.S.A.
        (602) 621-2018
        icon-project@arizona.edu     (Internet)
        ... {allegra, cmcl2, ihnp4, noao}!arizona!icon-project     (uucp)


   Please also let us know of any suggestions for improvements to
the porting process.

   Once you have completed your port, please send us copies of
any files that you modified so that we can make corresponding
changes in the central version of the source code. Once this is
done, you can get a new copy of the source code whenever changes
or extensions are made to the implementation.

   Also be sure to include documentation on any features that are
not implemented in your port or any changes that would affect
users.

Acknowledgements

   Many persons have been involved in the implementation of Icon.
Contributions to its portability have been made by Bill Mitchell,
Kelvin Nilsen, Gregg Townsend, and Cheyenne Wills.

References


1.   R. E. Griswold and M. T. Griswold, The Implementation of The
     Icon Programming Language, Princeton University Press, 1986.

2.   R. E. Griswold, Installation Guide for Version 7 of Icon,
     The Univ. of Arizona Tech. Rep. 88-6, 1988.

3.   R. E. Griswold, G. M. Townsend and K. Walker, Version 7 of
     Icon, The Univ. of Arizona Tech. Rep. 88-5, 1988.

4.   R. E. Griswold and M. T. Griswold, The Icon Programming
     Language, Prentice-Hall, Inc., Englewood Cliffs, NJ, 1983.

5.   R. E. Griswold, An Overview of the Icon Programming
     Language, The Univ. of Arizona Tech. Rep. 83-3, 1983.






                             - 20 -








6.   B. W. Kernighan and D. M. Ritchie, The C Programming
     Language, Prentice-Hall, Inc., Englewood Cliffs, NJ, 1978.

7.   Technical Committee X3J11, Draft Proposed American National
     Standard for Information Systems -  Programming Language C,
     Oct. 1986.

8.   R. E. Griswold, Version 7 of Icon for MS-DOS, The Univ. of
     Arizona Icon Project Document IPD47, 1988.
















































                             - 21 -








            Appendix A - Files Used by Components of Icon



Files marked by * are used in more than one component.

Files Used by itran

     config.h*  general configuration information
     define.h*  system-dependent definitions
     keyword.h* keyword definitions
     itran.h    general heading information of itran
     lex.h      header for lexical analysis
     lfile.h    header for link declarations
     sym.h      header for symbol tables
     token.h    token definitions
     tree.h     code tree information
     version.h* version information
     code.c     code generator
     err.c      error messages
     itran.c    main program
     keyword.c  keyword structure
     lex.c      lexical analyzer
     lnklist.c  file linking
     mem.c      memory management
     optab.c    state tables for operator recognition
     parse.c    parser
     sym.c      symbol table management
     toktab.c   token table
     tree.c     code tree constructor

Files Used by ilink

     config.h*  general configuration information
     cpuconf.h* computer architecture information
     define.h*  system-dependent definitions
     fdefs.h*   function definitions
     header.h*  icode header structure
     ilink.h    general heading information for ilink
     keyword.h* keyword definitions
     opcode.h   opcode structure
     opdefs.h*  icode instruction definitions
     paths.h*   file paths
     rt.h*      header for run-time system
     version.h* version information
     glob.c     processor for global information
     ilink.c    main program
     lcode.c    code generator
     llex.c     lexical analyzer
     lmem.c     memory management
     lsym.c     symbol table management
     opcode.c   opcode table





                             - 22 -








Files Used by iconx

     config.h*  general configuration information
     cpuconf.h* computer configuration information
     define.h*  system-dependent definitions
     fdefs.h*   function definitions
     gc.h       garbage collection definitions
     header.h*  icode header
     keyword.h* keyword definitions
     memsize.h* memory sizing
     opdefs.h*  icode definitions
     rt.h*      run-time definitions
     version.h* version information
     fconv.c    conversion functions
     fmisc.c    miscellaneous functions
     fscan.c    scanning functions
     fstr.c     string construction functions
     fstranl.c  string analysis functions
     fstruct.c  data structure functions
     fsys.c     system functions
     fxtra.c    extra functions
     idata.c    data
     imain.c    main program
     interp.c   icode interpreter
     invoke.c   function and procedure invocation
     lmisc.c    miscellaneous library routines
     lrec.c     library routines for record
     lscan.c    scanning routines
     oarith.c   arithmetic operations
     oasgn.c    assignment operations
     ocat.c     concatenation operations
     ocomp.c    comparison operations
     omisc.c    miscellaneous operations
     oref.c     referencing operations
     oset.c     set operations
     ovalue.c   value operations
     rcomp.c    comparison routines
     rconv.c    conversion routines
     rdefault.c default value routines
     rdoasgn.c  assignment routines
     rlocal.c   locally needed routines
     rmemexp.c  memory management routines for expandable regions
     rmemfix.c  memory management routines for fixed regions
     rmemmgt.c  general memory management routines
     rmisc.c    miscellaneous routines
     rover.c    arithmetic overflow routines
     rstruct.c  structure routines
     rswitch.c  co-expression context-switching routine
     rsys.c     system routines








                             - 23 -








Files Used by icont

     config.h*  general configuration information
     define.h*  system-dependent definitions
     paths.h*   path definitions
     icont.c    main program



















































                             - 24 -








               Appendix B - System-Dependent Code



   The following source files contain code that is operating-
system dependent.  The number of places where such code occurs in
each file is given in parentheses.

Translator:


        itran.c (5)


Linker


        ilink.c (7)
        lcode.c (2)
        llex.c (1)
        lmem.c (6)


Executor:


        fmisc.c (1)
        fsys.c (14)
        imain.c (10)
        interp.c (6)
        lmisc.c (6)
        rconv.c (2)
        rmemexp.c (2)
        rmemmgt.c (1)
        rmisc.c (1)
        rsys.c (2)


Command Processor


        icont.c (10)















                             - 25 -