Personalized Interpreters for Version
                           7 of Icon*


                        Ralph E. Griswold




                             TR 88-7

























                        January 22, 1988


                 Department of Computer Science

                    The University of Arizona

                      Tucson, Arizona 85721




*This work was supported by the National Science Foundation under
Grant DCR-8502015.













              Personalized Interpreters for Version
                            7 of Icon




1.  Introduction

   Despite the fact that the Icon programming language has a
large repertoire of functions and operations for string and list
manipulation, as well as for more conventional computations
[1,2], users frequently need to extend that repertoire. While
many extensions can be written as procedures that build on the
existing repertoire, there are some kinds of extensions for which
this approach is unacceptably inefficient, inconvenient, or sim-
ply impractical.

   Icon itself is written C and its built-in functions are writ-
ten as corresponding C functions. Thus, the natural way to extend
Icon's computational repertoire is to add new C functions to it.

   The Icon system is organized so that this is comparatively
easy to do.  Adding new functions does not require changes to the
Icon translator, since all functions have a common syntactic
form. An entry must be made in a table that is used by the linker
and the run-time system in order to identify built-in functions
and connect references to them to the code itself.

   One method of adding new functions to Icon is to add the
corresponding C functions to the Icon system itself and to
rebuild the entire system. This approach is impractical for many
applications. If the extensions are not of general interest, it
is inappropriate to include them in the public version of Icon.
On the other hand, Icon is a large and complicated system, and
having many private versions may create serious problems of
maintenance and disk usage. Furthermore, rebuilding the Icon sys-
tem is expensive. This approach therefore may be impractical in a
situation such as a class in which students implement their own
versions of an extension.

   To remedy these problems, a mechanism for building ``personal-
ized interpreters'' is included in UNIX* implementations of Icon.
This mechanism allows a user to add C functions and to build a
corresponding interpreter quickly, easily, and without the neces-
sity to have a copy of the source code for the entire Icon sys-
tem.

   To construct a personalized interpreter, the user must perform
                          
*UNIX is a trademark of AT&T Bell Laboratories.




                              - 1 -








a one-time set up that copies relevant source files to a direc-
tory specified by the user and builds the nucleus of a run-time
system. Once this is done, the user can add and modify C func-
tions and include them in the personalized run-time system with
little effort.

   Since the linker must know the names of built-in functions, a
personalized linker also is constructed. In order to run Icon
programs in a self-contained personalized run-time system, per-
sonalized versions of the translator, pitran, and the command
processor, picont, are provided also.

   The modifications that can be made to Icon via a personalized
interpreter essentially are limited to the run-time system: the
addition of new functions, modifications to existing functions
and operations, and modifications and additions to support rou-
tines. There is no provision for changing the syntax of Icon,
incorporating new operators, keyword, or control structures.


2.  Building and Using a Personalized Interpreter

2.1  Setting Up a Personalized Interpreter System

   To set up a personalized interpreter, a new directory should
be created solely for the use of the interpreter; otherwise files
may be accidentally destroyed by the setup process.  For the pur-
pose of example, suppose this directory is named myicon. The
setup consists of

        mkdir myicon
        cd myicon
        icon pi

Note that icon pi must be run from the area in which the person-
alized interpreter is to be built.  The location of icon pi may
vary from site to site.

   The shell script icon pi constructs three subdirectories: h,
std, and pi. The subdirectory h contains header files that are
needed in C routines. The subdirectory std contains the machine-
independent portions of the Icon system that are needed to build
a personalized interpreter.  The subdirectory pi contains a
Makefile for building a personalized interpreter and also is the
place where source code for new C functions normally resides.
Thus, work on the personalized interpreter is done in myicon/pi.

   The Makefile that is constructed by icon pi contains two
definitions to facilitate building personalized interpreters:

     OBJS a list of object modules that are to be added to or
          replaced in the run-time system. OBJS initially is
          empty.




                              - 2 -








     LIB  a list of library options that are used when the run-
          time system is built. LIB initially is empty, but the
          math library is loaded as a normal part of building the
          run-time system.

See the listing of the generic version of this Makefile in the
appendix.

2.2  Building a Personalized Interpreter

   Performing a

        make pi

in myicon/pi creates four files in myicon:

        picont     command processor
        pilink     linker
        piconx     run-time system
        piconx.hdr header file for linker output

Links to these files also are constructed in myicon/pi so that
the new personalized interpreter can be tested in the directory
in which it is made.

   The file picont normally is built only on the first make. The
file pilink is built on the first make and is rebuilt whenever
the repertoire of built-in functions is changed as a result of
modifications to h/fdefs.h.  The file piconx is rebuilt whenever
the source code in the run-time system is changed.

   The user of the personalized interpreter uses picont in the
same fashion that the standard icont is used.  (Note that the
accidental use of icont in place of picont may produce mysterious
results.) In turn, picont translates a source program using
pitran and links it using pilink.  The resulting icode file uses
piconx.

   The relocation bits and symbol tables in piconx can be removed
by

        make Stripx

in myicon/pi. This reduces the size of this file substantially
but may interfere with debugging.

   If a make is performed in myicon/pi before any run-time files
are added or modified, the resulting personalized interpreter is
identical to the standard one. Such a make can be performed to
verify that the personalized interpreter system is performing
properly.






                              - 3 -








2.3  Version Numbering

   The Icon run-time system checks an identifying version number
to be sure the linker and run-time system versions correspond.
The version number is the string defined for IVersion in
myicon/h/version.h following the construction of a personalized
interpreter as described in Section 2.1.

   In order to assure that files produced by pilink can only be
run by the current versions of piconx, the value of IVersion
should be changed whenever a change is made to a personalized
interpreter. It is not important what the definition of IVersion
is, so long as it is a short string that is different from previ-
ous ones.

2.4  Adding New Functions

   To add new functions to the personalized interpreter, it is
first necessary to provide the C code for them, adhering to the
conventions and data structures used throughout Icon [3].  The
directory src/iconx in the Version 7 Icon hierarchy [2] contains
the source code for the standard functions, which can be used as
models for new ones.

   Suppose that a function setenv is to be added to a personal-
ized interpreter.

   Four things need to be done to incorporate this function in
the personalized interpreter:

     1. Provide the code to the function (in, say, setenv.c).

     2. Add a line consisting of

                FncDef(setenv)

        to myicon/h/fdefs.h.  This allows the linker and the
        run-time system to know about the new function.

     3. Add setenv.o to the definition of OBJS in
        myicon/pi/Makefile.  This causes setenv.c to be compiled
        and the resulting object file to be loaded with the run-
        time system when a make is performed.

     4. Perform a make in myicon/pi. The result is new versions
        of pilink and piconx in myicon.

The function setenv now can be used like any other built-in func-
tion.

   More than one function can be included in a single source
file.  To incorporate these functions in a personalized inter-
preter, an FncDef entry needs to be added for each function, but
only the file need be added to the OBJS list.



                              - 4 -








2.5  Modifying the Existing Run-Time System

   The use of personalized interpreters is not limited to the
addition of new functions. Any module in the standard run-time
system can be modified as well.

   To modify an existing portion of the Icon run-time system,
copy the source code file from v7/src/iconx to myicon/pi.
(Source code for a few run-time routines is placed in myicon/std
when a personalized interpreter is set up. Check this directory
first and use that file, if appropriate, rather than making
another copy in myicon/pi.) When a source-code file in myicon/pi
has been modified, place it in the OBJS list just like a new file
and perform a make. Note that an entire module must be replaced,
even if a change is made to only one routine.  Any module that is
replaced must contain all the global variables in the original
module to prevent ld(1) from also loading the original module.
There is no way to delete routines from the run-time system.

   The directory myicon/h contains header files that are included
in various source-code files.  The file myicon/h/rt.h contains
declarations and definitions that are used throughout the run-
time system. This is where the declaration for the structure of a
new type of data object would be placed.

   Care must be taken when modifying header files not to make
changes that would produce inconsistencies between previously
compiled components of the Icon run-time system and new ones.

References

1. Griswold, Ralph E. and Madge T. Griswold. The Icon Programming
   Language. Prentice-Hall, Inc., Englewood Cliffs, New Jersey.
   1983.

2. Griswold, Ralph E.,  Gregg M. Townsend, and Kenneth Walker.
   Version 7 of Icon, Technical Report TR 88-5, Department of
   Computer Science, The University of Arizona. 1988.

3. Griswold, Ralph E. and Madge T. Griswold. The Implementation
   of the Icon Programming Language. Princeton University Press,
   Princeton, New Jersey. 1987.















                              - 5 -








         Appendix - Makefile for Personalized Interpreters




   The ``generic'' Makefile for personalized interpreters fol-
lows.  A copy, with the value of Dir filled in and appropriate
definitions for the flags, is placed in myicon/pi when icon pi is
run.

        SHELL=/bin/sh
        CFLAGS= -O
        LDFLAGS=
        XCFLAGS= -O
        XLDFLAGS= -N
        Dir=`pwd`
        Sdir=`pwd`/../pi


        RHDRS=    ../h/rt.h ../h/config.h ../h/define.h ../h/cpuconf.h ../h/memsize.h
        LHDRS=    ../std/ilink.h $(RHDRS)
        #
        #  To add or replace object files, add their names to the OBJS list below.
        #  For example, to add nfncs.o and iolib.o, use:
        #
        #         OBJS=nfncs.o iolib.o         # this is a sample line
        #
        #  For each object file added to OBJS, add a dependency line to reflect files
        #  that are depended on.  In general, new functions depend on $(RHDRS).
        #  For example, if nfncs.c contains new functions, use
        #
        #         nfncs.o:        $(RHDRS)
        #
        #  Such additions to this Makefile should go at the end.


        OBJS=
        LIB=


        RTOBJS=../std/imain.o ../std/rconv.o ../std/idata.o $(OBJS)


        Pi:       picont piconx pilink piconx.hdr


        picont:   ../std/icont.c ../h/config.h ../h/define.h ../h/paths.h
                  rm -f ../picont picont
                  $(CC) $(CFLAGS) -o picont -DItran="\"$(Dir)/pitran\""\
                          -DIconx="\"$(Dir)/piconx\"" \
                          -DIlink="\"$(Dir)/pilink\""  ../std/icont.c
                  strip picont
                  ln picont ../picont




                              - 6 -








        pilink:   ../std/linklib ../std/lsym.o ../std/ilink.o ../std/lcode.o ../std/lmem.o
                  rm -f ../pilink pilink
                  $(CC) $(LDFLAGS) -o pilink ../std/lsym.o ../std/ilink.o\
                           ../std/lcode.o ../std/lmem.o ../std/linklib
                  strip pilink
                  ln pilink ../pilink


        ../std/ixhdr.o:   ../h/config.h ../h/define.h
                  cd ../std;      $(CC) -c $(XCFLAGS) -DIconx="\"$(Sdir)/piconx\"" ixhdr.c


        piconx.hdr:       ../std/ixhdr.o
                  rm -f ../piconx.hdr piconx.hdr
                  $(CC) $(XLDFLAGS) ../std/ixhdr.o -o piconx.hdr
                  strip piconx.hdr
                  ln piconx.hdr ../piconx.hdr


        piconx:   ../std/rtlib $(RTOBJS)
                  rm -f ../piconx piconx
                  $(CC) $(LDFLAGS) -o piconx $(RTOBJS) ../std/rtlib $(LIB) -lm
                  ln piconx ../piconx



        ../std/idata.o:           $(RHDRS) ../h/fdefs.h fdefs.h
                  cd ../std;      $(CC) -c -DPI $(CFLAGS) idata.c


        ../std/imain.o:           $(RHDRS) ../h/header.h ../h/version.h ../std/gc.h \
                                     ../h/opdefs.h
                  cd ../std;      $(CC) -c $(CFLAGS) imain.c


        ../std/rconv.o:           $(RHDRS) ../h/fdefs.h fdefs.h
                  cd ../std;      $(CC) -c -DPI $(CFLAGS) rconv.c


        ../std/lsym.o:    $(LHDRS) ../h/fdefs.h fdefs.h
                  cd ../std;      $(CC) -c -DPI $(CFLAGS) lsym.c


        ../std/lmem.o:    $(LHDRS)
                  cd ../std;      $(CC) -c -DPI $(CFLAGS) lmem.c


        ../std/ilink.o:           $(LHDRS) ../h/header.h ../h/paths.h
                  cd ../std;      $(CC) -c $(CFLAGS) -DHeader="\"$(Sdir)/piconx.hdr\""  ilink.c








                              - 7 -








        ../std/lcode.o:           $(LHDRS) ../h/header.h ../h/paths.h ../std/opcode.h \
                                     ../h/keyword.h ../h/opdefs.h ../h/version.h
                  cd ../std;      $(CC) -c $(CFLAGS) lcode.c


        Stripx:   piconx
                  strip piconx


















































                              - 8 -